## Slide 1: Summary of RAN3 discussion status concerning NR on the topics for joint session with SA2 and RAN2
RAN3 NR Rapporteur (NTT DOCOMO, INC.)
3GPP TSG RAN WG2 meeting #92
Nanjing, China 23-27, May 2016
Agenda Item: 10.5
Document for: Discussion and decision
R3-161461

## Slide 2: Introduction
This document provides the rapporteur’s summary of RAN3 discussion status on the following agenda for the RAN2-RAN3-SA2 joint session for NR / NextGen
  RAN-CN interconnection variant
  RAN-CN functions
  Slicing
2

## Slide 3: RAN-CN interconnection variant
RAN3 Status:
  Proposed alternatives of RAN-CN connectivity's are reflected in RAN3 TR 38.801
  RAN3 to downs elect options in the next meetings
  NG1-C and NG1-U are the interfaces between NR and NG-core
  RAN3 has the Working Assumption that the interface between eLTE eNB and NG-Core is NG1
  The eLTE eNB is the evolution of eNB that supports connectivity to EPC and NG-Core
3
Does SA2 see the connection of NR BS to EPC to be part of SA2 work?
What is the role of EPC in 5G from a system architecture point of view?
Scenario1
Scenario2
...

## Slide 4: RAN-CN functions
RAN3 agreed to capture a list of NR RAN functions as follows
  Functions similar to E-UTRAN [TS 36.401] (see Table-1 in slide5)
  Additional functions that are agreed to be supported (see Table-2 in slide6)
  Additional functions which may be supported (see Table-3 in slide7)
  NOTE 1: The further detail of the functionalities needs further study
  NOTE 2: NR RAN refers to a RAN supporting NR. It may only consist of NR (standalone NR operation) or it may consist of NR and LTE (tight interworking) or it may consist of NR, LTE and WLAN (tight interworking).
4

## Slide 5: RAN-CN functions (1/3) Functions similar to E-UTRAN
Table-1: Functions similar to E-UTRAN [TS 36.401]
Transfer of user data
Radio channel ciphering and deciphering
Integrity protection
Header compression
Mobility control functions: Handover
Inter-cell interference coordination
Connection setup and release
Load balancing
Distributed function for NAS messages
NAS node selection function
Synchronization
Radio access network sharing
Paging
Positioning
5

## Slide 6: RAN-CN functions (2/3) Additional functions that are agreed to be supported
6
Table-2: Additional functions that are agreed to be supported (red text shows coordination pt with SA2) | 
Network Slice support | This function provides the capability for NR RAN to support network slicing
Interworking with LTE | This function provides tight interaction (e.g. DC) between NR and LTE
Multi-connectivity | This function provides means for connectivity between an NR node and multiple NR nodes
LTE-NR handover through LTE-NR interface | This function provides means for LTE-NR handover via the direct interface between LTE and NR.

## Slide 7: RAN-CN functions (3/3) Additional functions which may be supported
Table-3: Additional functions which may be supported (red text shows coordination pt with SA2) | 
UE operational mode during periods of no traffic | For instance, upon reception of DL data, RAN could notify the UE
NR location area management | This function provides the capability for NR RAN to manage location areas. It is FFS whether location area management needs to be coordinated with LTE.
RAN3 is dependent on RAN2 and SA2 on the above two functions | 
Direct services support | This function provides communication whereby UEs can communicate with each other directly
Interworking with non-3GPP systems | This function provides interworking between NR and Non-3GPP RAT (e.g. WLAN)
LTE-NR handover through CN | This function provides means for LTE-NR handover via the CN.
7

## Slide 8: Slicing
RAN3 agreed to capture the following key principles for support of Network Slicing in RAN
Key principle | Description (red text shows FFSes)
RAN awareness of slices | RAN shall support a differentiated handling of different network slices which have been pre-configured by the operator How RAN supports the slice enabling in terms of RAN functions (i.e. the set of network functions that comprise each slice) is implementation dependent It is still FFS if 3GPP will still additionally want to standardize a few basic slices and the network functions that comprise them (e.g. eMBB, MassiveMTC).
Network slice selection | RAN shall support the selection of the RAN part of the network slice by an index of ID provided by the UE which unambiguously identifies one of the pre-configured network slices in the PLMN How the UE gets this unambiguous index of ID is FFS and to be decided with SA2. The index or ID could be sent to the UE by the CN after the CN has selected the slice (e.g. similar to eDECOR feature) or it should be pre-configured in the UE. It is FFS how the RAN verifies that the UE is authorized to select the slice and when this verification happens It is FFS if the RAN may also select the slice based on specific resources accessed by the UE
Resource management between slices | RAN shall support policy enforcement between slices as per service level agreements How RAN handles the requirements coming from the service level agreements is to be discussed with SA2
Support of QoS | RAN shall support QoS differentiation within a slice It is FFS if RAN shall additionally support QoS enforcement independently per slice
RAN selection of CN entity (FFS) | RAN shall support initial selection of the CN entity for initial routing of uplink messages based on received slice index and a mapping in the RAN node (CN entity, slices supported) Need to discuss whether an NNSF-like function is needed that uses the slice index as input for initial selection of a CN entity that supports this slice
Resource isolation between slices (FFS) | RAN shall support resource isolation between slices Resource isolation needs to be clarified: It is unclear if resource isolation would imply that multiple slices cannot share control plane (respectively user plane) resources or processing resources in common. Its is unclear if resource isolation would imply that cryptographic means should be used to isolate CP and UP traffic between slices.
8