## Slide 1: Summary of offline discussion on CU-DU QoS handling
NTT DOCOMO, INC.
R3-180606
3GPP TSG RAN WG3 NR Adhoc meeting
January 22nd – 25th, 2018 Sophia Antipolis, France

## Slide 2: Tasked work for come back
CB: # 59_CUDU_QoS_Handling
- Who decides DRB QoS config? (CU or DU)
- What happens with multiple flows within the same DRB?
- clarify functionality and relationship with QoS handling as currently defined
- merge comments from all treated papers
(NTT)
Summary of Offline Disc on CU-DU QoS Handling R3-180606

## Slide 3: Point of discussion
Through offline discussion with companies, it was clarified that the point of discussion is
  Whether CU provides to DU, QoS profile for each DRB and/or for each flow in a DRB
    Where QoS profile to be provided consists of 5QI, ARP, Non-standardized QoS flow descriptor, GBR QoS flow information (or parts thereof)

## Slide 4: Alternatives
Following alternatives have been proposed
  Alt.1: CU provides to DU, QoS profile for each flow
    I.e., CU takes QoS profile info for each flow received over NG, and just forwards them as-is to DU
  Alt.2: CU provides to DU, QoS profile for each DRB
    I.e., CU takes QoS profile info for each flow received over NG, determines an “aggregate QoS profile” for each DRB, and forwards them to DU
  Alt.3: CU provides to DU, QoS profile for each flow and DRB
    I.e., Alt.1 plus Alt.2
Note that
  It is common to all alternatives that QoS granularity at DU are DRBs, and there is only one “aggregate QoS profile” for a DRB
  So in essence, the difference between the alternatives is only about who (CU and/or DU) determines the “aggregate QoS profile” for a DRB from the individual QoS profiles for each flows mapped to a DRB

## Slide 5: Reasoning/Justification
Reasoning/justification provided by the proponents
  Alt.1
    DU is in better position to determine “aggregate QoS profile” for a DRB, since DU implementation (e.g. scheduler and L1/L2 configuration) is strictly linked to QoS that can be served
  Alt.2
    Since in the end, DU only applies one “aggregate QoS profile” for a DRB, there is no point in transferring individual QoS profiles for each flows mapped to a DRB
  Alt.3
    It allows both CU and DU to have some control over “aggregate QoS profile” for a DRB

## Slide 6: Proposal
Continue in RAN3#99 to discuss the 3 alternatives and their reasoning / justification captured in this document to reach a conclusion