## Slide 1: Way Forward on n5B 25MHz aggregated BW MSD
Skyworks Solutions, Inc., Qualcomm
3GPP TSG-RAN WG4 Meeting # 100-e R4-2114900
Electronic Meeting, Aug. 16-27, 2021

## Slide 2: Background
Uplink CA_n5B maximum aggregated bandwidth of 25MHz has been recently requested for BCS1 [1]
Single Uplink and Dual-Uplink MSD test points have been proposed in in R4-2114579 [2] for symmetric UL/DL 25 MHz aggregated CBW,
  Concerns have been raised that for single carrier 25MHz downlink operation, uplink CBW is restricted to 20MHz.
  It has therefore been requested to first reach agreement on the MSD test points configuration. Based on these agreements, companies could then bring MSD data at the next meeting.

## Slide 3: Proposed Way Forward
Proposal 1: The following CA_n5B uplink PCC/SCC CBW configurations are agreed to evaluate the MSD for BCS1 25MHz aggregated CBW.
Proposal 2: Interested companies are requested to bring MSD analysis for CA_n5B BCS1 25MHz maximum aggregated BW to RAN4#101 based on the uplink configuration above. Other RB allocations are not precluded for MSD analysis.
CA configuration | SCS (kHz) | Channel bandwidth (PCC+SCC) | UL PCC allocation | UL SCC allocation | PCC IMD order | SCC IMD order | Comment
 | (PCC/SCC) | (MHz) | (LCRB) | (LCRB) |  |  | 
CA_n5B | 15/15 | 20 + 5 | 16 (RBstart = 90) | 4 (RBstart = 0) | IMD5 | IMD3 | SCC: near complete IM3 overlap
 |  | 15 + 10 | 12 (RBstart = 67) | 8 (RBstart = 0) | IMD5 | IMD3 | 
 |  | 15 + 5 | 15 (RBstart = 64) | 5 (RBstart = 0) | IMD5 |  | greater PCC overlap than SCC
 |  | 10 + 10 | 10 (RBstart = 42) | 10 (RBstart = 0) | IMD5 |  | greater SCC overlap than PCC

## Slide 4: References
[1] NR CA and DC Request for RAN4 #100e_ATT, 3GPP TSG-RAN WG4 Meeting # 100-e, AT&T
[2] CA_n5B MSD, 3GPP TSG-RAN WG4 Meeting # 100-e, Skyworks Solutions, Inc.