## Slide 1
On Demodulation Evolution and Enhancements Topics for Rel-19
3GPP TSG-RAN WG4 Meeting #110 R4-2401720
Athens, Greece, 26 Feb – 01 Mar, 2024
Agenda Item: 14
Document for: information
Huawei, HiSilicon

## Slide 2
Demodulation performance enhancement for 8Rx
Soft-IC for SU-MIMO

## Slide 3
Demodulation performance enhancement for 8Rx
Soft-IC for SU-MIMO
Demodulation evolution and enhancements

## Slide 4
Performance enhancements for 8Rx capable UE
Motivation
  RAN4 has defined the performance requirements with MMSE-IRC receiver for suppressing inter-cell interference and intra-cell inter-user interference for 2Rx and 4Rx for FR1 in Release 17 (RP-221285)
    Slot-based transmission and aligned SCS among cells
    MMSE-IRC with DMRS based interference covariance estimation
  RAN4 introduced the performance requirements with MRC/MMSE-IRC without interference assumption for 8Rx in Release 18 (RP-230314)
  There are no performance requirements for 8Rx with MMSE-IRC with interference assumption
  The performance for MIMO layer not less than 4 is verified under limited scenarios
Objective
  Define PDSCH performance requirements with MMSE-IRC receiver for suppressing inter-cell interference for 8Rx with MIMO layer not less than 4 for FR1
  Define PDSCH performance requirements with MMSE-IRC receiver for suppressing intra-cell inter-user interference for 8Rx for FR1
  Define the enhanced demodulation performance requirements with MIMO layers not less than 4 layers for 8Rx capable UE
    Investigate the scenarios under which the performance needs be verified

## Slide 5
Soft-IC for SU-MIMO
Motivation
  NR UE demodulation performance under the medium correlation channel can be improved by introducing the soft IC receiver to cancel the inter-stream interference for SU-MIMO scenario, which does the iteration abstracting the soft information and cancelling the interference from each other between multiple layers by involving LDPC decoder.
  The soft IC receiver can bring the performance gain not only over MMSE receiver but also over RML receiver.
    It is observed that the performance could be improved by around 1.5 to 3dB using soft-IC receiver under the medium correlation channel.
Objective
  Specify performance requirements for the advanced receiver with soft IC to cancel the inter-stream interference for single-cell multi-layer scenario
    Evaluate the performance gain of the advanced receiver with soft IC compared to existing NR receiver(s)
    Specify PDSCH requirements for the advanced receiver with soft IC