## Slide 1
3GPP TSG-RAN WG4 Meeting #72 R4-145538
Dresden, Germany, 18 – 22 August 2014
Source: TeliaSonera
Title: WF on B42 and B43 UE co-existence
Agenda item: 4.2.1.1
Document for: Approval
___________________________________________________________________________
In order to enable un-synchronised operation between B42 and B43 and in-band the following cases shall be considered (for ~3.5 GHz):
With NS_01 for B42 and B43:
1) For ≤ ΔfOOB follow existing general SEM mask
For > ΔfOOB it will follow -30 dBm/MHz (no A-MPR is needed)
No actions required for this in the specifications as it can be already fulfilled
With NS_22 for B42 and B43:
2) -23dBm/5MHz at 5MHz offset from the aggressor over a 20 MHz region
-40dBm/MHz at 25 MHz offset from the aggressor to the end of the band
There will be a note saying: For adjacent carriers in B42 and B43 the emission limit could imply risk of harmful interference to UE(s) operating in the protected operating band.

## Slide 2
20MHz E-UTRA
General SEM
-30dBm/MHz
ΔfOOB
The NS/A-MPR following shall protect B42/B43 UE-coexistence and in-band for these bands:
Case 1: Use existing NS_01 and general spurious emission requirements of -30 dBm/MHz, no A-MPR and no changes in specification needed
Case 2: Define A-MPR required for new SEM within ΔfOOB range and extended SEM for >ΔfOOB
20MHz E-UTRA
General SEM
-30dBm/MHz
ΔfOOB
Case 1) With NS_01 for B42 and B43:
20MHz E-UTRA
-23dBm/5MHz
-40dBm/MHz
5MHz
offset
25MHz
20MHz E-UTRA
-23dBm/5MHz
-40dBm/MHz
5MHz
offset
25MHz
Case 2) With NS_22 for B42 and B43: