## Slide 1: WF on layer 3 and 4 demodulation requirements
Huawei, Hisilicon, MediaTek, Intel, Qualcomm, Ericsson, ZTE
R4-155127
TSG RAN WG4 meeting #76
Beijing, China, 24-8 Aug, 2015
Agenda Item: 7.8.4.1

## Slide 2: Way forward
Layer 3 or(and) 4 PDSCH test cases will be introduced as test requirements in R.13 4RX WI:
  Demodulation tests with fading channel
    TM3 (FFS)
    TM4
    TM9
  SDR test(s) with static channel
    TM3
    TM4 (FFS)
Test purpose is to verify the UE’s implementation at least on the following aspects
  MIMO receiver
  layer-to-codeword mapping
  Channel estimation and rate-matching of DMRS port 9/10 for DMRS-based transmission
  High layer pre-coding matrix for TM3 /TM4 demodulation
  High layer PMI measurement and reporting for TM4/TM9 (FFS)

## Slide 3: Assumptions ( for information)
companies are encourage to bring more analysis and evaluation based on the following assumptions
  Demodulation tests
Transmission mode | TM3 | TM4 | TM9
Bandwidth | 10MHz |  | 
Scheduled PRB | 50PRB |  | 
CCH symbol | 1 or 2 |  | 
Antenna configuration | Option 1: 4x4 low Option 2: 4x4, New medium cross-polarized for 3 layer |  | 
Propagation channel | EVA70 | EPA5 | EPA5
CRS configuration | Port 0,1,2,3 | Port 0,1,2,3 | Port 0,1
DMRS configuration | - | - | Port 7,8,9,10
CSI-RS configuration | - | - | Port 15,16,17,18
scheduled subframe | [1 2 3 4 6 7 8 9] |  | 
CSI feedback | - | PUCCH 1-1 | PUCCH 1-1
Beamforming model | - | Followed wideband PMI | Followed wideband PMI
Layer number | Option 1: Layer 3; Option 2: Layer 4 |  | 
MCS | Option 1: [MCS14]; Option 2: 256QAM for TM9 Option3: others |  | 

## Slide 4: Assumptions ( for information)
  SDR test(s)
Transmission mode | TM3/TM4
Bandwidth | 10MHz/20MHz
Scheduled PRB | 50PRB/100PRB
CCH symbol | 1
Antenna configuration | 4x4
Propagation channel | AWGN*
CRS configuration | Port 0,1,2,3
DMRS configuration | -
CSI-RS configuration | -
scheduled subframe | [1 2 3 4 6 7 8 9]
Overhead | -
CSI feedback | -
Beamforming model | -
Layer number | 4 layers
Modulation order | 64QAM/256QAM
Coding rate | TBD
* It is encouraged to also specify the 4x4 AWGN channel used in the simulation