## Slide 1: Way forward on RS-SINR measurement
CMCC, Intel, Ericsson, Nokia
3GPP TSG-RAN WG4 Meeting #76
Beijing,China, Aug 23~Aug 28, 2015
R4-155139

## Slide 2: SINR definition
RSRP and interference part of SINR is measured only on CRS REs of the target cell.
Interference estimation of SINR is not compensated for different UE receiver types.

## Slide 3: SINR definition
This definition is for simulation purpose (R4-154494)
Agree on the SINR definition next meeting and send LS to RAN1 and RAN2.
RS-SINR is defined as the linear average over the power contribution (in W) of the resource elements carrying CRS divided by the linear average of the noise and interference power contribution (in W) of the resource elements carrying CRS within the considered measurement frequency bandwidth.
For RS-SINR determination, the cell-specific reference signals R0 according TS 36.211 shall be used. If the UE can reliably detect that R1 is available it may use R1 in addition to R0 to determine RS-SINR.
The reference point for the RS-SINR shall be the antenna connector of the UE.
If receiver diversity is in use by the UE, the reported value shall not be lower than the corresponding RS-SINR of any of the individual diversity branches.

## Slide 4: Link level simulation
Companies are encouraged to provide link level simulation results to evaluate the accuracy requirements of RS-SINR for next meeting.
Link level simulation assumptions:

## Slide 5: System level simulation
Interested companies are encouraged to provide system level evaluation for next meeting.
The system level simulation assumptions are provided in R4-154570.
Other system level simulation assumptions are not precluded for evaluation, e.g. inter-frequency evaluation.

## Slide 6: For information
  Cell specific Reference Signal Signal to Noise and interferer Ratio (CRS-SINR) is defined as the ratio RSRP/(CRSRERP-RSRP) The measurements in RSRP and CRSERP shall be made over the same resource elements.
  RSERP is the average resource element power received at the antenna connector in time and frequency domain where cell specific reference symbols are transmitted on the target cell and RSRP is the RSRP of the target cell
  RSRP and CRSERP are measured only from OFDM symbols containing reference symbols for antenna port 0 of measurement subframes.
  The reference point for the CRS-SINR shall be the antenna connector of the UE.
  If receiver diversity is in use by the UE, the value of RSRP shall not be lower than the corresponding RSRP of any of the individual diversity branches and CRSRERP shall be measured on the same antenna branch as RSRP.
SINR definition (Ericsson, R4-154568)

## Slide 7: For information
CRS-SINR = RSRP/([CRS-RSSI] - RSRP)
Where:
  Reference signal received power (RSRP), is defined as the linear average over the power contributions (in [W]) of the resource elements that carry cell-specific reference signals within the considered measurement frequency bandwidth
  E-UTRA CRS Carrier Received Signal Strength Indicator (CRS-RSSI), comprises the linear average of the total received power (in [W]) of the resource elements that carry cell-specific reference signals within the considered measurement frequency bandwidth, including co-channel serving and non-serving cells, adjacent channel interference, thermal noise etc.
  RSRP and CRS-RSSI are measured only from REs containing reference symbols for antenna port 0 of measurement subframes.
  The reference point for the CRS-SINR shall be the antenna connector of the UE.
  If receiver diversity is in use by the UE, the reported value of CRS-SINR shall not be lower than the corresponding CRS-SINR of any of the individual diversity branches.
SINR definition (Nokia)