## Slide 1: Wayforward on SFN and subframe offset reporting for DC enhancement
Intel, Ericsson, NTT DOCOMO, CATT
R4-155194
3GPP TSG-RAN WG4 #76
Beijing, China, Aug. 24th – Aug. 28th, 2015
Agenda Item: 7.9.3.1

## Slide 2: Wayforward
SFN and subframe timing difference (SSTD) measurement report comprises of 3 elements:
SFN offset between MeNB and SeNB (X)
    X = SFNPCell – SFNPSCell where:
      SFNPCell and SFNPSCell are SFN numbers of PCell and PSCell respectively.
    Reporting range of X : [-511, 512) in frame number
Frame boundary offset between MeNB and SeNB (Y)
    Y = TFrameBoundaryPCell - TFrameBoundaryPSCell, where
      TFrameBoundaryPCell is the time of PCell frame start
      TFrameBoundaryPSCell is the time of PSCell frame start closest to that of PCell
    Reporting range of Y : [-4, 5] in subframe number
Subframe boundary offset between MeNB and SeNB (Z)
  The received time difference between MeNB and SeNB at the UE, defined as Z = TSubframePCell-TSubframePSCell, where:
    TSubframePCell is the time when the UE receives the start of one subframe from PCell and
    TSubframePSCell is the time when the UE receives the corresponding start of one subframe from PSCell that is closest in time to the subframe received from PCell.
  The maximum possible value of can vary between -500 µs and +500 µs. However the UE will report Z over a limited reporting range.
    The reporting range is FFS; RAN4 will provide details about reporting range in RAN4#76bis