## Slide 1: WF on DL Control Channel IM for Asynchronous networks
Intel Corporation, ZTE, NTT DOCOMO, Ericsson
3GPP TSG-RAN WG4 Meeting #77 Anaheim, CA, US, 16 – 20 Nov, 2015
Agenda Item: 7.4
R4-158376

## Slide 2: Way Forward (1)
FFS whether enhanced performance requirements are introduced for the DL control channel IM receivers in the asynchronous networks
Companies are encouraged to bring more analysis on the achievable performance and robustness for the DL control channel IM receivers in the asynchronous networks in the next meeting

## Slide 3: Way Forward (2)
Candidate reference IM receiver for PDCCH/PCFICH/PHICH in asynchronous networks is LMMSE-IRC
Interference model for asynchronous network scenarios
  Baseline: 1/3 and 2/3 subframes as timing offset for the 2 NCs (i.e. same as for Rel.11 MMSE-IRC).
    Other configurations are not precluded
  Interference structure
    Option 1: Reuse interference model from Rel-11 Type A receiver requirements
    Option 2: Define a new interference model
      Full or partial interference PDSCH loading.
        PRB-level partial interference loading may be taken into consideration.
      Full or partial interference PDCCH/PHICH/PCFICH region loading.
        Power boosting is also not precluded

## Slide 4: Simulation Assumptions (1)
Companies are encouraged to bring simulations in the next RAN4 meeting for the following test cases to assess the performance gains and robustness of the enhanced IM receiver structures
The results are expected to be provided for the following reference receiver structures
  LMMSE-MRC, LMMSE-IRC
Note: Companies can bring additional results for scenarios not listed in the WF to assess the feasibility of receivers
# | Control channel | INR | Network Type | Duplexing
1 | PDCCH / PCFICH | High Medium | Asynchronous | FDD
2 | PHICH | High Medium | Asynchronous | FDD
3 | EPDCCH | High Medium | Asynchronous | FDD

## Slide 5: Simulation Assumptions (2)
Parameters | Value
System bandwidth | 10MHz for both serving cell and interfering cells
Duplexing mode | FDD
Cyclic prefix | Normal
Number of interference cells | 2 interfering cells
Interference power profile | High INR: I1/Noc = 13.91 dB, I2/Noc = 3.34 dB Medium INR (I1/Noc = 7.77 dB, I2/Noc = 2.29 dB)
Network synchronization scenarios | Time offset: 1/3 and 2/3 subframes as timing offset for the 2 NCs Frequency offset: 0 Hz between all cells
CRS ports | Port 0 and 1
Antenna configuration | 2x2 with Low correlation
Tx EVM | 6%
Unused Serving cell RE-s and PRB-s | OCNG
Interference model for asynchronous scenario | Rel-11 Type A receiver asynchronous interference model (TS 36.101 B.5.2) Companies can provide results for additional scenarios
Channel model | EVA70
Number of PHICH groups (Ng) | 1
PHICH duration | Normal

## Slide 6: Simulation Assumptions (3)
Parameters | Value
PDCCH/PCFICH parameters | 
Serving cell PDCCH | AL 2, 4; DCI Format 2 (43 bits – FDD, 10MHz)
CFI | CFIS = 3, CFII = 3
Performance metrics | Pm-dsg vs SINR
PHICH parameters | 
PHICH FRC | R.19 in TS 36.101
CFI | CFIS = 1, CFII = 1
Performance metrics | Pm-an vs SINR
EPDCCH parameters | 
Serving cell EPDCCH | FRC #1: AL 2 Localized EPDCCH FRC #2: AL 4 Distributed EPDCCH DCI Format 2C (44 bits – FDD, 10MHz)
Number of PDCCH symbols and EPDCCH start | CFIS = CFII=2, EPDCCH starting symbols is derived from CFI
EPDCCH parameters | Number of EPDCCH Sets Configured = 1 Distributed EPDCCH set PRBs {3, 17, 31, 45} Localized EPDCCH set PRBs {0, 7, 14, 21, 28, 35, 42, 49} EPDCCH is transmitted in all subframes EPDCCH precoding model is in accordance to TS 36.101 B.4.4. and B.4.5
Performance metrics | Pm-dsg vs SINR