## Slide 1: Way forward on NPBCH Performance Requirements
Intel, Qualcomm, Samsung, Ericsson, LGE
3GPP TSG-RAN WG4 Meeting #80bis
Ljubljana, Slovenia, 10 - 14 Oct, 2016
R4-168737

## Slide 2: Background
In RAN4 #80, it was identified that Rel-13 NPBCH performance within 1-MIB TTI appeared not enough to achieve the given target SNRs.
RAN1 assumes a NB-IoT UE to try multiple N-MIB TTIs to acquire N-MIB information, accordingly RAN4 investigates the N-MIB acquisition time.
In RAN4 #80bis, RAN4 considers if the acquisition time is introduced as one of NPBCH test conditions to achieve the target SNRs.

## Slide 3: N-MIB Acquisition Time Observations
Based on the study proposals in R4-167085, RAN4 observed the following based on simulation results in RAN4 80bis
    [3~10] TTIs of 640ms are required for N-MIB acquisition with target SNR = -12dB
Test Case | Config | Huawei | E/// | ZTE | QC | CATT | Samsung | Nokia | Intel
1 | EPA-1Hz 1X1 1% BLER | -2.8dB (1TTI) | -4.5dB (1TTI) -10.5dB (10TTI) | -5.1 (1TTI) -9.6 (2TTI) -11.7dB (3TTI) | -7dB (1TTI) -12.1(4TTI) -12.5(5TTI) -13.1(6TTI) | -3.9 (1TTI) -6.8 (2TTI) -8.6 (3TTI) | -3.3dB (1TTI) |  | -4.5 (1TTI) -11.5 (4TTI) -12.4 (5TTI) -13.0 (6TTI)
2 | EPA-1Hz 2X1 1% BLER | -8.1dB (1TTI) -10.7dB (2TTI) -12 dB (3TTI) | -7.5dB (1TTI) -12.1dB (10TTI) | -8.2dB (1TTI) -12.4dB (4TTI) | -8.5 (1TTI) -12.5(4TTI) -12.7(5TTI) -13.1(6TTI) | -5.8 (1TTI) -7.9 (2TTI) -9.7 (3TTI) | -6.1dB (1TTI) | -6.6dB (1TTI) | -8.0 (1TTI) -12.5 (4TTI) -13.0 (5TTI) -13.5 (6TTI)

## Slide 4: Multiple N-MIB TTI acquisition Window
NPBCH Performance Requirement
NPBCH BLER target is 1%
N-MIB acquisition time is taken into account for the NPBCH demod performance requirement at the target SNR.
  The N-MIB acquisition time length, ‘W’, is selected in integer steps of 640ms (see page 3)
  The pm-bch is defined for each NPBCH decoding attempt within ‘W’
  The receiver characteristics of NPBCH for UEs supporting coverage enhancement are determined by the probability of miss-detection of the NPBCH (Pm-bch), which is defined as
    Where A is the number of keep trying intervals (640ms) with at least one successfully decoded N-MIB PDU and B is the total number of keep trying intervals.
  ‘W’ value is determined based on the results with RF impairments

## Slide 5: WF on NPBCH Performance Requirements
Test case #1 : Single N-MIB TTI acquisition window
  W = 1
Test case #2 : Multiple N-MIB TTI acquisition window (see page 4)
  NPBCH demod performance requirement should achieve the target SNR (-12dB)
  W is TBD (W > 1). W is derived based on simulation results in a way to reach target SNR
Both ‘Test case #1’ and ‘Test case #2’ are introduced in TS36.101 NPBCH requirement.
Companies are encouraged to bring simulation and impairments results for NPBCH to derive the SNR requirements and ‘W’ value in RAN4 #81.
  A single TTI NPBCH performance for test case #1
  Multiple N-TTI acquisition window ‘W’ for test case #2