## Slide 1: Way Forward on additional issues related to multi-node tests for LAA
Ericsson, Qualcomm Incorporated, Huawei, Nokia, Verizon, …
3GPP TSG-RAN WG4 Meeting #80Bis R4-168893
Ljubljana, Slovenia, 10-14 October, 2016

## Slide 2: Background (1)
In RAN4#80 and RAN4#79, two way forwards [1], [2] on multi-node tests have been agreed.
Two tests has been agreed, namely:
  Throughput test (related to channel access priority class 3)
  Outage test (related to channel access priority class 1)
[1] R4-166971, WF on LAA Multi-node test
[2] R4-164971 WF on LAA co-existence testing

## Slide 3: Background (2)
Meeting notes from two evening adhocs are attached here

## Slide 4: Choice of devices
All 802.11 devices should be commercially available and not reference design
IEEE 802.11 APs and STAs, should be selected from multiple vendors and multiple generations of the 802.11 standard.
  Devices shall be selected from 802.11n and 802.11ac.
For LAA:
  LAA BS supplied by vendors
  LAA UEs should be representative “commercially available” or “ready for market”
Agreed

## Slide 5: Test Setup
Note: as updated in TP: R4-16xxxx
The following test setup is assumed to be a baseline for further discussions:
Circulator needed here
Small details remain

## Slide 6: Test cases
Note: as detailed in revised TP
Other traffic cases are FFS
The purpose of the test when WiFi is the aggressor is to help 3GPP to validate LAA and enhancement of system performance; there will be no pass/fail criterial for WiFi (AGREED)
Scenario | Victim system |  | Aggressor system |  |  |  | Traffic Type for both victim and aggressor
 | Victim device to be tested | Companion victim device | Aggressor device in baseline | Companion aggressor device | Aggressor device to be tested | Companion aggressor device | 
1 | Wi-Fi AP | Wi-Fi STA | Wi-Fi AP | Wi-Fi STA | LAA BS | LAA UE | Best effort
2 | Wi-Fi AP | Wi-Fi STA | Wi-Fi AP | Wi-Fi STA | LAA BS | LAA UE | Voice
3 | LAA BS | LAA UE | LAA BS | LAA UE | Wi-Fi AP | Wi-Fi STA | Best effort
4 | LAA BS | LAA UE | LAA BS | LAA UE | Wi-Fi AP | Wi-Fi STA | Voice
Table to be discussed

## Slide 7: Traffic cases
WiFi to WiFi best effort
  Best effort WiFi  best effort WiFi
  Best effort WiFi  VoIP WiFi
LAA to WiFi best effort
  Best effort LAA  best effort WiFi
  Best effort LAA  VoIP WiFi
WiFi to WiFi VoIP
  VoIP WiFi  VoIP WiFi
  VoIP WiFi  best effort WiFi
LAA to WiFi best effort (for LAA devices that support VoIP)
  VoIP LAA  VoIP WiFi
  VoIP LAA  best effort WiFi
WiFi will use bi-directional voice traffic
Best effort traffic will be full buffer UDP
NOTE: Other traffic cases are FFS
To be discussed
(6 and 7 together)

## Slide 8: Device parameter settings
The tests shall ensure repeatability and representative operational behavior.
The starting point of the configuration of both 802.11 and LAA equipment shall be based on the default settings.
In order to achieve the test objectives of repeatability and representative operational behavior, modifications to the default settings might or might not be needed
The above modifications, if needed, are FFS
Modifications compared to the defaults settings, if any, shall be documented
Agreed

## Slide 9: Throughput Tests: Rx levels (current proposals)
Proposed RX levels in dBm
  -72+∆1 and -82-∆2 (R4-168545)
  -62+∆ and -82-∆ (R4-167653)
  -62 ±∆ and -82 ±∆ (R4-165830)
  -62 and -82 (R4-168405)
  -57dBm, -67dBm, -77dBm, -82dBm(R4-167941)
No agreement
Include the proposals in TP

## Slide 10: Throughput Tests: target operating point (current proposals)
SNR/SINR/SIR levels
  SINR=15dB (R4-168545)
  SNR=16dB (R4-167653)
  SIR=15dB (R4-165830)
  SIR=0dB (R4-167941)
  SINR = 0dB(R4-168405)
No agreement
Include the proposals in TP

## Slide 11: Throughput Tests: pass fail criteria (current proposals)
Pass fail criteria
  Median of recorded throughput CDF (R4-168545)
  Mean of the recorded throughput CDF (R4-165830)
  Normalized best effort throughput and at {5%ile, 25%ile, 50%ile, 75%ile, 95%ile} (R4-167941)
  Mean of the recorded throughput CDF (R4-168405)
Accuracy for pass/fail criteria
  10%
More than one pass/fail criteria can be considered
Under consideration

## Slide 12: Outage test
Similar to throughput test
  Test setup
  Choice of devices
  RX levels
  Operating point
Traffic cases
  VoIP traffic in both links
Pass/fail criteria:
  What is the metric?
    What percentage of packets lost within a period of time? How many times of burst packet loss? i.e. 3 consecutive packets lost within certain time?
    Jitter
    Latency
Under consideration