## Slide 1
3GPP TSG-RAN WG4 #78bis
San José Del Cabo, México, 11-15 April, 2016
Agenda item: 7.13.3
LG Electronics
WF for list of RRM core requirement
R4-161832

## Slide 2: Impacted List of RRM core requirement
 | title | Impacted by |  | Comment
 |  | GNSS | High speed | 
4.5.2.2 | Interruptions with ProSe Direct Communication | No | No | 
4.5.2.4 | Initiation/Cease of SLSS transmissions with ProSe Direct Communication | No | Yes | Need to study impact on Tevaluate,SLSS(# of DRX cycle)
7.16.2.1 | ProSe UE transmission timing | Yes | No | Need to consider GNSS as timing reference
7.16.3.2 | Interruptions at ProSe Direct Communication configuration | No | No | 
7.16.3.5 | Interruptions during ProSe Direct Communication | No | No | 
7.16.5 | Selection / Reselection of ProSe relay UE | No | No | 
8.10.2.2 | Initiation/Cease of SLSS transmissions with ProSe Direct Communication | No | Yes | Need to study impact on Tevaluate,SLSS(# of DRX cycle)
11.2 | UE Transmit Timing for ProSe in Any Cell Selection State | Yes | No | Need to consider GNSS as timing reference
11.3 | Initiation/Cease of SLSS Transmissions | No | No | 
11.4 | Measurements for ProSe in Any Cell Selection State | No | No | 
11.5 | Selection / Reselection of ProSe Synchronization Reference | No | No | 
11.7 | Selection / Reselection of ProSe relay UE | No | No | 

## Slide 3: WF of RRM on V2V
GNSS based synchronization should be considered in the RRM core requirement for PC5-based V2V.
  GNSS should be added as timing reference.
  Timing error should be specified for timing reference of GNSS.
High speed of vehicle should be considered in the RRM core requirement for PC5-based V2V.
  Evaluation time of SLSS should be studied under high speed, i.e. 250km/h, for initiation/cease of SLSS transmission
Except for above requirements, existing RRM core requirements can be reused for PC5-based V2V.