## Slide 1: Way forward on EARFCN for NB-IoT
Huawei, Ericsson, CMCC, …
3GPP TSG-RAN WG4 Meeting #78bis R4-162814 San Jose del Cabo, Mexico, 11 – 15 April, 2016

## Slide 2: Background
Carrier frequency and RF channel numbering are discussed for NB-IoT. [1][2]
RAN1 informed the restricted carrier transmitting NPSS/NSSS for in-band and guard band operations for the downlink, as well as the possible flexible carrier frequency for the uplink. [3]
Multi-carrier NB-IoT is introduced in RAN1.[4]
[1] R4-162302, “On RF channels for NB-IoT”, Huawei
[2] R4-162244, “Carrier frequency and EARFCN for NB-IoT”, Ericsson
[3] R4-161311, “Reply LS on channel raster for NB-IoT”, RAN WG1
[4] R4-162700, “LS on NB-IoT”, RAN WG1

## Slide 3: Proposals
Carrier frequency and RF channel number need to be defined for NB-IoT.
Carrier frequency FDL_loT for the downlink is defined as,
  FDL_loT = FDL_low + 0.1(NDL – NOffs-DL) + 0.0025*(2MDL+1), where
  FDL_low , NDL and NOffs-DL reuse the Table 5.7.3-1 of both TS36.104 and TS36.101.
  NDL is the EARFCN that corresponds to NB-IoT and is different than the value that corresponds to LTE downlink carrier frequency.
  MDL= -10,-9,-8,-7,-6,-5,-4,-3,-2,-1,-0.5,0,1,2,3,4,5,6,7,8,9 represent all of the possible offset of NB-IoT channel number to EARFCN
    Note: for the carrier including NPSS/NSSS, MDL is selected from {-2,-1,-0.5,0,1}.
Carrier frequency FUL_loT for the uplink is defined as,
  FUL_loT = FUL_low + 0.1(NUL – NOffs-UL) + 0.0025*(2MUL), where
  FUL_low , NUL and NOffs-UL reuse the Table 5.7.3-1 of both TS36.104 and TS36.101
  NUL is the EARFCN that corresponds to NB-IoT and is different than the value that corresponds to LTE uplink carrier frequency.
  MUL= -10,-9,-8,-7,-6,-5,-4,-3,-2,-1,0,1,2,3,4,5,6,7,8,9 represents all of the possible offset of NB-IoT channel number to EARFCN
Send LS to RAN2 to inform the definition for NB-IoT.
  RAN4 ask RAN2 to consider the above carrier frequency and RF channel number definition for NB-IoT into their work.