## Slide 1: WF on LAA Bandwidth combination sets in CA basket work items
Nokia, […..]
R4-162906

## Slide 2: Reference
Treated already in RF session
R4-162164 Inclusion of 10MHz CBW for LAA operation, Ericsson
R4-162279 Bandwidth combination sets for LAA, Nokia
R4-162298 Discussion on channel bandwidth for LAA, Huawei
R4-162294 Considerations on adding 10MHz channel bandwidth for CA combinations with Band 46, Huawei
R4-162647 Addition of 10 MHz channel bandwidth for LAA, Qualcomm
R4-162280 WF on LAA Bandwidth combination sets in CA basket work items, Nokia
Not treated yet in RF session
R4-162605 LAA 10MHz, Vodafone

## Slide 3: Wayforward
10MHz is included in Band 46 in Rel-14.
CAs are release independent from Rel-13.
10MHz channels
  Is it enough to cover 5825-5875MHz? FFS for the next meeting.
  BCS
    Introduce 10MHz to 3+46 and 7+46 as BCS1 in the next meeting.
      BCS0 is already completed. Other bands can be proceeded with BCS0
    Introduce 10MHz to CA_46C and CA_46D as BCS1
      BCS0 is reserved for fallback operations without 10MHz.
36 40 44 48 52 56 60 64
5150 5250 5350 5470 5570 5725 5825 5875 5925
Channel number
Wifi
100 104 108 112 116 120 124 128 132 136 140
149 153 157 161 165 169
LAA in R13
20MHz
10MHz