## Slide 1: WF on measurement gap enhancement
Intel, [Ericsson, Huawei, Nokia, Qualcomm]…
3GPP TSG-RAN WG4 Meeting #79 R4-163277
Nanjing, China 23 – 27 May, 2016

## Slide 2: Shorter MGL for synchronous operations
Requirements for Short MGL will only be defined when all intra- and inter-frequency cells are synchronized in frame level with receive time misalignment less than X us. The value of X is for further study.
Requirements for inter-RAT measurement will not be defined when reduced gaps are configured
Shorter MGL configurations
  MGL: 3ms or 4ms
    The above shorter MGL configurations subject to maintain current UE measurement requirements. If evaluation and analysis suggest these configurations can not maintain the current UE requirement, these configurations needs to be revised.
  MGRP: 40ms and 80ms

## Slide 3: Per-CC based measurement gap configuration
Two type of new measurement gap configurations are considered
  Uniformly distributed measurement gap pattern, e.g. legacy gap liked
  Non-uniformly distributed measurement gap pattern, e.g. burst gap
If Uniformly distributed measurement gap pattern with MGL=6ms and MGRP>80ms are introduced
  new MGRP should be divisible by 40ms
  10240ms should be divisible by new MGRP
  Open issues :
    number of new equal-distance measurement gap configurations
    corresponding MGRP
Measurement gap may or may not be configured per CC based
It is FFS whether new gap configurations are introduced (uniform and/or non uniform)

## Slide 4: Per-CC based measurement gap configuration
Some Options for capability signaling:
  Option 1: UE signals capabilities for all supported CA combos when UE attaches to the network
  Option 2: UE signals capabilities on demand(network advertises what it supports and UE replies with related capabilities)
  Option 3: UE signals capabilities based on configured CA combo(UE sends capabilities when configured with a certain CA combo)
  Option 4: UE picks the gap configuration when the measurement configuration is received from network
  Other options are not precluded
  The discussion on capability signalling option may take place in RAN2
The capability signaling for per CC gap should consider the use case of spare RF chains, and NCSG potentially being provided on other CC
For RAN4#80, interested companies are invited to consider what information needs to be provided to RAN2 about UE RF architecture options to allow them to specify capability signaling

## Slide 5: NCSG and interruption control
NCSG configurations
  For synchronous operations where receive time misalignment is less than X us. The value of X is for further study
  VIL-ML-VIL: 1-4-1 (DL) and 1-4-2(UL)
    VIRP:
      Option 1: 40ms
      Option 2: 40ms and 80ms
  It is FFS for asynchronous operations where receive time misalignment exceeds X us