## Slide 1: Way forward on transmit timing accuracy for CE Mode B
Qualcomm
3GPP TSG-RAN WG4 Meeting #80
Göteborg, Sweden 22-26 August, 2016
R4-166835

## Slide 2: Background
Transmit timing accuracy for Rel-13 eMTC (as defined in 36.133 Section7)
  CE Mode A: ±24 Ts
  CE Mode B: FFS
UE needs to spend additional power to maintain timing accuracy, especially during DRX operation
  UE needs to perform early wake-up (turn on and monitor DL) before DRX ON duration to achieve timing accuracy during DRX ON
  As signal quality degrades, duration of early wake-up increases, so does power consumption
  In CE mode B, SNR can be as low as -15dB, hence wake-up durations can be potentially very long
Relaxation of accuracy
  Impact to UE: Potentially significant power saving (needs investigation)
  In context of NB-Iot, timing accuracy relaxed to ±80Ts
  For eMTC, this way-forward proposes to evaluate the impact of relaxation of accuracy requirements in CE mode B on duration of early wake-up in UEs

## Slide 3: Evaluation & Simulation assumption
Metric of evaluation: Number of subframes (N) required to achieve timing accuracy (T_final) given an initial timing accuracy (T_init)
Companies are encouraged to bring evaluations based on the above table. Other channels are not precluded for evaluation
Parameter | 
Sys BW | 10MHz
Duplex Mode | FDD
Channel | AWGN, ETU1
SNR | -15dB
Antenna Configuration & Correlatiom | 2x1 low
UE initial timing error (T_init) | ±120Ts, ±96Ts
UE initial frequency error | 100Hz (can be more depending on LO ppm assumptions)
Target T_final | ±72Ts, ±48Ts, ±32Ts, ±24Ts