## Slide 1: Way forwards on eMTC UE demodulation requirements
Ericsson
3GPP TSG-RAN WG4 Meeting #80
Göteborg, Sweden 22-26 August, 2016
R4-166996

## Slide 2: PBCH demodulation requirements
Observation
  RAN4 has discussed the demodulation performance of PBCH and observed a gap between the required SNR for 1% PBCH decoding error rate and the target SNR (-15dB) of MPDCCH demodulation performance requirements.
  It is not possible to increase the repetition of PBCH beyond the MIB TTI of 40ms.

## Slide 3: PBCH demodulation requirements
PBCH simulation parameters are updated to quantify the performance of the “keep trying” algorithm in the PBCH demodulation test by introducing the keep trying window, such that:
  The “keep trying” decoder is definition is:
    In this solution, there are no standard changes required. The decoder simply “keeps trying” to decode the normally transmitted PBCH frames until the decoder eventually gets lucky and decodes it correctly. With this solution there is a trade-off between coverage gain and decoding time (i.e. the number of decoding attempts). [Refer to R1-132908]
  The keep trying window length, W, is defined in integer steps of 40 ms (40 ms, 80 ms, …)
  The pm-bch for Cat-M1 UE is defined for each PBCH decoding attempt within W

## Slide 4: PBCH demodulation requirements
Interested companies are encouraged to provide the PBCH simulation results based on the following parameters in order to set the performance requirement for PBCH at the same CE Mode B test point as MPDCCH
Parameters | Case 1 | Case 2 | Case 3 | Case 4
System bandwidth | 10MHz | 10MHz | 10MHz | 10MHz
Propagation condition | EPA1 | EPA1 | ETU1 | ETU1
Antenna configuration and correlation matrix | 2x1 low | 2x1 low | 2x1 low | 2x1 low
Repetition of PBCH | Disabled | Enabled | Disabled | Enabled
W (NOTE 1) [ms] | {40, 640} | {40, 160} | {40, 640} | {40, 160}
UE Frequency error [Hz] | 100 | 100 | 100 | 100
Target SNR (dB) | -12 | -12 | -12 | -12
NOTE 1: Companies are encouraged to select other values for W in order to meet the target SNR |  |  |  | 

## Slide 5: MPDCCH Precoding weight update granularity assumption
Specify the cell specific parameter (Frequency hopping interval) in the MPDCCH demodulation requirement parameters regardless of the frequency hopping enable to provide UE assumption on precoding granularity. (TS36.211).
Precoder update granularity of the actual transmission should be matched with the frequency hopping interval

## Slide 6: MPDCCH demodulation requirements
PDSCH transmission modes used for MPDCCH test
  CE Mode A:
    TM2 for CE Mode A: 29bits for FDD, 32bits for TDD
  TM2 for CE Mode B: 18bits for FDD/TDD
Interesting companies are encouraged to provide the simulation results for FDD and TDD including impairment error in RAN4#80bis.

## Slide 7: Scheduling pattern for MPDCCH demodulation requirements
Use the following scheduling pattern
  N1+1+6 [ms] periodicity
    N1 for repetition number for MPDCCH
    1 for gap between the end of MPDCCH and the beginning of PDSCH
    6 for switching gap between DL and UL, and UL transmission
  Set the PDSCH repetition number to 1

## Slide 8: PDSCH demodulation requirements
Introduce a new TM2 PDSCH demodulation requirements
  Same setting as TM6 demodulation requirements
  No repetition
  Applicability: UE not supporting CE Mode B
Interesting companies are encouraged to provide the simulation results for FDD and TDD including impairment error in RAN4#80bis.

## Slide 9: CQI definition test
Test points:
  SNR=5/6dB
  Interesting companies are encouraged to bring issues in RAN4#80bis if they find issue on these test points.

## Slide 10: UE-selected subband CQI test
Companies are encouraged to provide the simulation results to verify the R4-166826 in RAN4#80bis

## Slide 11: Open issues
Refer to R4-166997