## Slide 1: WF on Measurement Accuracy for NB-IoT
Nokia, [Huawei], [HiSilicon], [DoCoMo], [Ericsson], [Intel], [ZTE], [CMCC], [Qualcomm]
R4-167118
3GPP TSG-RAN WG4 #80
Göteborg, Sweden, 22 – 26 August, 2016
Agenda Item: 6.7.3.1

## Slide 2: Measurement accuracy results (RAN4#80)

## Slide 3: Way Forward
For next meeting RAN4#80bis companies are encouraged to bring simulation results:
  Inband scenario
  Enhanced coverage
  Normal coverage
  Stand-alone scenario
Results should be without margins
  RAN4 will discuss the margin separately

## Slide 4: Way forward
RAN4#80bis should agree on accuracy numbers for:
  Normal Coverage measurement accuracy:
    NRSRP: -+[TBD]dB
    NRSRQ: -+[TBD]dB
  Enhanced Coverage measurement accuracy:
    NRSRP: -+[TBD]dB
    NRSRQ: -+[TBD]dB
  Margins
RAN4 should decide whether separate requirements will be defined for in-band and stand-alone/guard-band?

## Slide 5: Way forward
In RAN4#80bis meeting:
  Decide on the measurement periods:
    [400]ms for normal coverage
    [800]ms for enhanced coverage
  Agree on final measurement periods for NB-IoT normal and enhanced coverage.

## Slide 6: measurement accuracy simulation assumption
Following parameters need to be included in the assumptions for alignment of results:
Frequency error:
  +/- 50Hz @2 GHz
Minimum number of subframes containing NRS per L1 measurement period used by the UE for NRSRP/NRSRQ measurements:
  For L1 measurement period of 400 ms: 30 subframes containing NRS
  For L1 period of 800 ms: 60 subframes containing NRS
  Time window over which coherent combining is done is to be disclosed by the companies for alignment purpose.
Measurement periods in non-DRX: 400 ms (normal coverage) and 800 ms (enhanced coverage)
Measurement accuracy requirements derived for maximum value obtained at the 5th and 95th percentiles of CDF

## Slide 7: Simulation assumptions for RRM measurement