## Slide 1: WF on UE Beamforming Model for the ITU WP5D coexistence simulations
Qualcomm
R4-167123
3GPP TSG-RAN WG4 Meeting #80
Aug 22nd – 26th, 2016, Gothenburg, Sweden

## Slide 2: General Antenna Model
Antenna consists of Mg x Ng panels, each of them composed of M x N antenna elements
P polarizations are used (in the example below P=2)
Mg
Ng

## Slide 3: Back ground – RAN1 agreements from chairman notes in RAN1#85
For UE with (Mg, Ng) directional antenna panels.
  Introduce (Ωmg,ng, Θmg,ng) for orientation of the panel (mg, ng), 0≤mg<Mg, 0≤ng<Ng, where the orientation of the first panel (Ω0,0, Θ0,0) is the same as UE orientation, Ωmg,ng is the array bearing angle and Θmg,ng is the array downtilt angle defined in [TR 36.873].
  For NR MIMO evaluation:
    Config 1: (Mg, Ng) = (1, 2); Θmg,ng=90; Ω0,1=Ω0,0+180; (dgH, dgV)=(0,0)
    Config 2: (Mg, Ng ) = (1, 4); Θmg,ng=90; Ω0,1=Ω0,0+90; Ω0,2=Ω0,0+180; Ω0,3=Ω0,0+270; (dgH, dgV)=(0,0)
    Other configurations can have panel specific position offset (dgH, mg, ng, dgV, mg, ng). Note in this case the notation of (Mg, Ng) does not leads to rectangular shape.
  UE orientation for mobile device (Ω0,0, Θ0,0)=(U(0,360), 90); UE orientation for customer premise equipment (CPE) can be optimized
  Each antenna array has shape dH=dV=0.5λ
    Config 1 can be used with config a/b; Config 2 can be used with config c/d/e
    Config a: (M, N, P) = (2, 4, 2), the polarization angles are 0 and 90
    Config b: (M, N, P) = (4, 4, 1) , the polarization angle for even panel is 0 and for odd panel is 90
    Config c: (M, N, P) = (2, 2, 2), the polarization angles are 0 and 90
    Config d: (M, N, P) = (2, 4, 1) , the polarization angle for even panel is 0 and for odd panel is 90
    Config e: (M, N, P) = (1, 4, 2), the polarization angles are 0 and 90
    FFS: Other configurations, e.g. (M, N, P) = (4, 4, 2) or (M, N, P) = (4, 8, 1) can be considered for 70GHz band, without exceeding the limit on the maximum number of UE antenna elements
  The antenna elements of the same polarization of the same panel is virtualized into one TXRU
  FFS: one TXRU can connect to different subarrays dynamically
  Note: The channel coefficients for each UE panel can be generated using spatial channel model
Companies should describe the method used for TRP association with UE-side beamforming

## Slide 4: WF on RAN4 UE antenna assumption for the ACI coexistence study
The following configuration should be used as default configuration for the coexistence study:
  Single panel is used, i.e. Mg=Ng=1. This configuration is adopted to simplify the simulation process
  UE orientation:
    random orientation in the azimuth domain: uniformly distributed between -90 and 90 degrees*.
    fixed elevation: 90 degrees
  (M, N) = (2,2)
  dH=dV=0.5λ
  P = 2
    Polarization is taken into account by adding 3dB to the beam forming gain
  Element gain:
    Element gain including losses: 5dBi
    Vertical and Horizontal 3dB bandwidth 3dB = 90 degrees, i.e. =90ͦͦͦ° and =90°
    Am= 25dB
    SLAV=25dB
  Beam forming:
    Single beam is created with the same linear phase progression as the one adopted for BS beam forming
* NOTE: This is done to emulate two panels: the configuration is equivalent to 2 panels with 180 shift in horizontal orientation and UE orientation uniformly distributed in the azimuth domain between -180 and 180 degrees