## Slide 1: Way forward on BS RF requirements for NR
Agenda Item: 10.5.3
Document for: Approval
Source: Nokia, Ericsson, Huawei
3GPP TSG-RAN WG4 #80bis Tdoc R4-168796
Ljubljana, Slovenia, 10th – 14th October 2016

## Slide 2: Background
21 contributions were discussed in agenda item 10.5.3 in the NR session
This contribution summaries the issues and agreed WF for BS RF requirements
WF on NF is discussed in separate contribution R4-158770

## Slide 3: NR BS output power
BS Output power accuraccy requirement be EIRP or TRP approximation or both
  TRP approximation with low measurment complexity may have a different name to TRP (currently discussed in eAAS WI)
  In case ACLR is agreed with TRP approximation, it should be noted that there would be no additional measurement complexity to measure also TRP output power
  FFS whether EIRP alone is suitable for regulating co-channel and adjacent channel interference

## Slide 4: NR BS output power
BS classification related power limit
  Investigate further the options for setting the max power limit for the BS class
    TRP only
    EIRP (in the main beam) only
    Both TRP and EIRP (in the main beam)
Reference condition
  BS is generally tested under worst case conditions, in most cases this is the maximum power condition (particularly important for EVM, ALCR, spurious emission, etc). The maximum power condition must be known so that it can be used when testing the other requirements
  The maximum output power as reference condition is FFS

## Slide 5: BS unwated emissions
Further investigations recommended in following areas
  Carrier-centric SEM or the band/carrier-centric UEM principle
  Choice of border between OOB and spurious domain
  Choice of absolute or relative levels
  Choice of actual value for ACLR requirement
  Follow ACLR agreement; intention is to use new name for TRP metric
Following principles are considered for defining the ”mask”
  FCC limits for mmWave bands as a starting point
  The absolute limits should be defined for NR
  Boundary may not be aligned with the ITU-R recommendation. Instead, it should depend on the channel BWs adopted by NR and the band filter rejection capability

## Slide 6: BS spurious emissions
Both Category A and Category B emission limits should be defined for NR bands above 6GHz
2nd harmonic should be considered as upper limit of frequency range for measurements of spurious emissions for NR bands above 13GHz
26GHz should be considered as upper limit of frequency range for measurements of spurious emissions for NR bands between 6GHz and 13GHz
How to define OTA requirements, and whether to define the conductive requirements for NR bands below 6GHz is FFS
  Above 6GHz also to be considered
TRP or EIRP metric is an open issue

## Slide 7: BS ACLR
Based on new definiton approved in eAAS WF (R4-168872)
The core requirement to be defined as OTA ACLR according to the definition in R4-168872
Open issues for consideration for coming meetings, to be discussed in eAAS session:
  Define possible measurement sampling grids required for OTA ACLR and other in-band unwanted emissions
  Determine if the measurement sampling grid for OTA ACLR and other in-band unwanted emission can be aligned with the desired signal sampling grid
  Define concepts on how to define the region corresponding to the intended base station coverage area and the desired/wanted outside this area in order to further reduce the number of measurement points
  The power over sphere (Pd, Pe) has been referred to as TRP in many papers, this term is not acceptable and an alternative will be defined. Suggestions for an alternative term are encouraged

## Slide 8: BS EVM
EVM for UE specific beam is defined in the centre of the main beam
The declarations approach from AAS can be used to clarify how the EVM requirement is met
NR can follow the same approach as AAS for defining test configurations for EVM
The criteria for allowed value to be decided later
Based on eAAS WF (R4-168873)

## Slide 9: BS classes
Too early to conclude on BS classes
As the requirements for the NR become more clear, identify where requirement applicability and values differ and then discuss whether the differences should be captured by means of defining further BS classes, or by some other means
Further discussion is needed on whether to capture
  simulation parameter (like MCL today) for each BS class in the TS as means of describing deployment scenarios
    Minimum distance from BE to UE could be one option
  simulation assumptions behind the BS class dependent requirements by some other means
  parameters based on EIRP considering the cell sizes
  whether to define different BS classes for below 6GHz or above 6GHz or both is FFS

## Slide 10: BS testability aspects (1)
Consider and develop a framework that differentiates BSs based on operating frequency and ability to use beamforming
OTA requirements for frequencies above 6 GHz
  whether to define conducted requirements above 6 GHz is FFS
Conducted requirements on current bands below 6 GHz not exploiting beamforming extensively (e.g. RRU + passive antenna)
BS operating at current bands or possible new bands below 6 GHz exploiting beamforming (e.g. AAS base stations), both OTA requirements and hybrid requirements would be necessary
Maximize the synergies considering experiences captured in the AAS and eAAS work when the NR requirement framework is developed

## Slide 11: BS testability aspects (2)
The following is a provisional list of RF requirements identified for further discussion on testability:
  Transmit:
    Output power, EVM, frequency error, other signal quality requirements, ACLR, in band unwanted emissions, out of band and spurious emissions, TDD TX OFF power and transient time, TX intermodulation, EMC
  Receive:
    Minimum & reference sensitivity, in band blocking, out of band blocking, RX intermodulation, RX spurious emissions, EMC