## Slide 1: 3GPP TSG-RAN WG4 Meeting #81 Reno, Nevada, USA, 14 – 18 November 2016
Huawei, Nokia, [Ericsson], [ZTE], Samsung
Way forward on NB-IoT BS demodulation performance
R4-1610559

## Slide 2: Background
During RAN4#80bis meeting, WF R4-168720 about NB-IoT BS demodulation performance was approved.
How to define the final NB-IoT BS demodulation performances needs to be finalized in RAN4#81.

## Slide 3: Margin
Add the STD from ideal results to companies’ averaged values with impairments as the final NB-IoT BS demodulation performance requirements.
  The STD should be 2dB if larger than 2dB
Please refer to R4-1609438 “Summary for NB-IoT BS simulation results” for the detailed STD values from ideal results.

## Slide 4: NPRACH Requirements
Case | AVE of Results with impairments | STD from ideal results | Final Requirements
AWGN 0Hz Rep8 | -3.2 | 1.1 | -2.1
AWGN 0Hz Rep32 | -7.8 | 1.0 | -6.8
EPA1 200Hz Rep8 | 5.2 | 0.9 | 6.1
EPA1 200Hz Rep32 | -0.1 | 0.6 | 0.5
Final NPRACH performance requirement shall be set as per the following “Final Requirements” values with square bracket

## Slide 5: NPUSCH format 1 Requirements
Case | AVE | Extra margin | Final Requirements
3.75KHz rep1 | -2.1 | 0.2 | -1.9
3.75KHz rep16 | -10.2 | 1.0 | -9.2
3.75KHz rep64 | -13.6 | 1.4 | -12.2
15KHz single-tone rep1 | -2.6 | 0.2 | -2.4
15KHz single-tone rep16 | -8.4 | 0.5 | -7.9
15KHz single-tone rep64 | -12 | 0.6 | -11.4
15KHz multi-tone12 rep2 | -0.9 | 0.8 | -0.1
15KHz multi-tone12 rep16 | -8.6 | 1.2 | -7.4
15KHz multi-tone12 rep64 | -13.1 | 1.4 | -11.7
15KHz multi-tone6 rep2 | -1.2 | 0.5 | -0.7
15KHz multi-tone6 rep16 | -9 | 1.1 | -7.9
15KHz multi-tone6 rep64 | -12.2 | 1.1 | -11.1
15KHz multi-tone3 rep2 | -4.6 | 0.6 | -4.0
15KHz multi-tone3 rep16 | -8.3 | 0.9 | -7.4
15KHz multi-tone3 rep64 | -10 | 0.9 | -9.1
Final NUSCH format 1 performance requirement shall be set as per the following “Final Requirements” values with square bracket
Note: AVE: average of results with impairments; Extra margin: STD from ideal results

## Slide 6: NPUSCH format 2 Requirements
Case | AVE of results with impairments | STD of ideal results | Final Requirements
3.75KHz rep1 | 5.0 | 2.1->2.0 | 7.0
3.75KHz rep16 | -7.2 | 1.9 | -5.3
3.75KHz rep64 | -12.9 | 2.5->2.0 | -10.9
15KHz single rep1 | 5.2 | 1.1 | 6.3
15KHz single rep16 | -5.6 | 1.7 | -3.9
15KHz single rep64 | -11.5 | 2.1->2.0 | -9.5
Final NPUSCH format 2 performance requirement shall be set as per the following “Final Requirements” values with square bracket