## Slide 1: Way forward on NR BS requirements prioritization for mm wave
R4-1610575, Ericsson

## Slide 2: Prioritization of requirements for mm wave
Two priorities are identified for requirements for mm wave
  Priority 1: Priority 1 requirements will be addressed first during the Rel-15 WI phase as they form an essential minimum set of requirements
  Priority 2: Priority 2 requirements will be addressed once priority 1 requirements are solved. It is possible that priority 2 requirements will be completed in a later release than Rel-15.
The aim in the study item is to discuss and indicate a potential prioritization. The prioritization can be re-visited and altered later if needed. The WI will decide separately whether to follow the prioritization.

## Slide 3: Prioritization of requirements for mm wave (TX)
Requirement category | Priority | Reason for priority
Channel numbers | 1 | New channel numbers are essential for the new bands at higher frequencies.
EIRP accuracy | 1 | Basic beamforming requirement already existing for other systems
Unwanted emissions | 1 | Including operating band and spurious emission in terms of absolute emissions Essential for regulatory compliance and proper coexistence
In band emissions | TBC | 
Transmit inter-mod | 2 | Needed for co-location, not essential for coexistence.
Signal quality | 1 (EVM, regulatory signal quality e.g. frequency error) 2(non regulatory signal quality) | EVM is a basic essential requirement to ensure that the transmitter works properly Assumption is that frequency error is needed for regulatory requirements It should be checked whether TAE is really needed and relate to regulatory requirements at mm wave.
Transmitter dynamics | 2 | 
Transmitter ON/OFF power & time | 1 | Essential for a TDD system to work properly
Beam domain | FFS | Requirement not yet identified; will be addressed based on R4-1610576

## Slide 4: Prioritization of requirements for mm wave (RX)
Requirement category | Priority | Reason for priority
Receiver sensitivity | 1 | Basic requirement for the receiver.
Receiver blocking | 1 | Essential for ensuring that co-existence works properly
Receiver intermodulation | 1 | 
Receiver dynamics | 1 | 
Receiver spurious emission | 1 | Assumption is that this is needed for regulatory requirements; could be changed if regulatory requirements would later not need this.
Receiver in-channel selectivity | 1 | 
Receiver performance | 2 | Not essential for regulatory, coexistence or basic performance.