## Slide 1: Simulation assumptions for SI acquisition for NB-IoT
Ericsson, Intel
3GPP TSG-RAN WG4 Meeting #81
Reno, Nevada, USA, 14-18, November, 2016
Agenda item: 5.6.4
R4-1610599

## Slide 2: MIB-NB/SIB1-NB/SIB2-NB acquisition
MIB-NB TTI = 640ms
SIB1-NB TTI = 2560ms
SIB2-NB TTI is up to eNB scheduling
Candidate algorithms to acquire MIB-NB/SIB1-NB/SIB2-NB
  Baseline: The “keep trying” decoder is definition is: The decoder simply “keeps trying” to decode the transmitted NPBCH frames until the decoder eventually gets lucky and decodes it correctly. With this solution there is a trade-off between coverage gain and decoding time (i.e. the number of decoding attempts). [Refer to R1-132908]
  Other algorithms are not precluded
MIB-NB/SIB1-NB/SIB2-NB acquisition delay = 99%-ile of the number of frames required to successfully decode the MIB-NB/SIB1-NB/SIB2-NB
To obtain MIB-NB/SIB1-NB/SIB2-NB acquisition delay, companies are encouraged to provide CDF of MIB-NB/SIB1-NB/SIB2-NB acquisition time based on the simulation results in the following slides
All the impairment margin such as DC leakage should be considered

## Slide 3: Simulation assumption for MIB-NB acquisition in RRM core requirements
 | Case 1 Normal coverage | Case 2 Enhanced Coverage
Number of NRS ports {1,2} | 2 | 2
Propagation channel | EPA1 | EPA1
Modulation | QPSK | QPSK
Coding rate | 50/1600 | 50/1600
Payload (without CRC) | 34 bits | 34 bits
Target SNRs | -6dB | -12dB

## Slide 4: Simulation assumption for SIB1-NB acquisition in RRM test
 | Case 1 Normal coverage | Case 2 Enhanced Coverage
Deployment mode | In-band | In-band
Number of NRS ports {1, 2} | 2 | 2
Propagation channel | EPA1 | EPA1
I_TBS {0/3/6/9} = {208/328/440/680bits} | 208bits | 208bits
Repetition number {4 ,8, 16} | 16 | 16
Target SNRs | -6dB | -12dB

## Slide 5: Simulation assumption for SIB2-NB acquisition in RRM test
 | Case 1 | Case 2
Deployment mode | In-band | In-band
Number of NRS ports {1, 2} | 2 | 2
Propagation channel | EPA1 | EPA1
TBS (si-TB-r13) | 208bits | 208bits
Number of SF {1,2,…,8,10} | 8 | 8
Si-WindowLength(*) | 160 | 960
Si-RepetitionPattern (*) | every2ndRF | every2ndRF
Target SNRs | -6dB | -12dB
(*) Refer to TS36.331 V.13.3.0 5.2.3a