## Slide 1: WF on how to determine ACLR/ACS from ACIR for WP5D
NTT DOCOMO, Inc.
3GPP TSG-RAN WG4 Meeting #81
Reno, US, 14 - 18 Nov, 2016
R4-1610621

## Slide 2: Back ground
In legacy study, basically
  BS ACLR was derived from ACIR with UE ACS
  BS ACS was derived from ACIR with UE ACLR
    ACIR was derived from co-existence study
In NR, there are discussion that we need to consider how to make balance between ACS of UE and ACLR of BS and vice versa.

## Slide 3: Way forward
Companies, especially UE venders and BS venders, are encouraged to provide information on feasible UE ACLR/UE ACS and/or BS ACLR/BS ACS
  ACLR and ACS for WP5D are determined taking into account following manner.
  Proposed ACLR/ACS should meet following:
    [1 / ( (1/ACLR) + (1/ACS) )] is equal to the determined ACIR.
  Feasibility provided by companies should be taken into account

## Slide 4: WF: Time schedule
(1) Companies provide ACIR derived from simulation results (by Dec. 23)
(2) Companies, especially UE venders and BS venders, provide information on feasible UE ACLR/UE ACS and/or BS ACLR/BS ACS. (by Jan. 10)
  (3) Companies propose BS ACLR/UE ACS for DL and UE ACLR and BS ACS for UL, and determine ACLR/ACS for WP5D (by Jan. 10)
(4) Based on the determined ACS/ACLR, reply LS are discussed (in #AH meeting).
Note: (2) is done in parallel with (1)