## Slide 1: WF on V2V power imbalance tests
LGE, Huawei, HiSilicon, Qualcomm Inc., Ericsson, CATT, Intel, …
3GPP TSG-RAN WG4 Meeting #81 Reno, Nevada, USA, 14 - 18 November, 2016
Agenda Item: 8.19.4.2
R4-1610701

## Slide 2: Background
During Rel-12, Power imbalance test for D2D was introduced [R4-155118]
  The purpose of power imbalance test is to check the demodulation performance when receiving PSSCH transmissions from two sidelink UEs with large power imbalance in one subframe.
For information, following methodology was used for power imbalance of Rel-12 D2D
  The target requirement ICS = -21 dBc depends on IBE
  Select SINR2 from simulation results for decoding SNR@70% throughput point.
  Select SNR2 such that SNR2 >> SINR2 (e.g., 5dB higher)
  Compute SNR1 from the relation: SINR2 = SNR2 – 10*log10(10^((SNR1 + ICS)/10)+1).

## Slide 3: Background
For Rel-14 V2V, PSCCH is always transmitted with its scheduled PSSCH with 3 dB higher PSD.
  Link 1 will be more affect on Link 2 receiving performance.

## Slide 4: Way Forward
Agree on introducing power imbalance test for V2V demodulation requirements
  Reuse existing D2D methodology as baseline
  Once ICS and SINR2 values are decided, SNR1 and SNR2 value can be calculated by agreed equation.
How to handle 3 dB boosted PSCCH impact
  Option 1. Consider modified SNR calculation equation
    SINR2 = SNR2 – 10*log10(α * 10((SNR1+ICS)/10) + 1)
      α = (2*NPRB-PSCCH+NPRB-PSSCH)/(NPRB-PSCCH+NPRB-PSSCH)
  Option 2. Use non-adjacent PSCCH/PSCCH transmission
  Option 3. Other options is not precluded.

## Slide 5: Way Forward
ICS(In-Channel Selectivity) values
  Option 1. Reuse existing D2D ICS value of -21 dBc.
  Option 2. Defer until IBE requirement is finalized in RF room.
  Other options are not precluded.
In next meeting, interesting companies are encouraged to propose specific ICS value based on analysis.

## Slide 6: Simulation assumptions
In next meeting, interesting companies are encouraged to submit simulation results to decide SINR2 values
  Detailed test configuration including Tx Fo/To parameters will be discussed in next meeting.
V2V Test/Simulation parameter | Proposals
 | To evaluate SINR2 for power imbalance
AGC settling time1 | QPSK: 1 symbol
Tx EVM | 10%
Propagation channel | Static : H = [ 1; 1]
Doppler spectrum | N/A
Relative Timing & Frequency error (considering Tx and Rx) | [12] Ts / [600] Hz
HARQ retransmissions2 | [0]
PSSCH RMC | [3] PRB with MCS10 (QPSK, R=2/3)
Performance metric | SNRPSSCH @ x% [BLER]/[Throughput]
Note 1. Not used for demodulation Note 2. Soft-combining is used if HARQ retransmission is used |