## Slide 1: Way forward on CQI reporting performance under SFN scenario
NTT DOCOMO, INC., Huawei
3GPP TSG-RAN WG4 Meeting #81 R4-1610714 Reno, Nevada, United States, 14th Nov 2016 - 18th Nov 2016

## Slide 2: Background
The CSI part of the high speed enhancement WI was identified as follows,
  Specify new CSI requirements considered for the final solutions to enhance the downlink demodulation performance if needed.

## Slide 3: Way Forward
First, RAN4 investigate whether CQI test is needed.
  The feasibility of defining the CQI test is investigated.
    Variation of the reporting CQI index
      The trajectory can be provided.
    Performance( reporting CQI distribution and throughput ) gap between legacy CQI measurement with HST UE and new CQI behavior UE.
      Any new CQI measurement behavior of HST UE should be identified for test introduction.
  Investigate if CQI measurement improvement can be verified from demodulation performance improvement aspect.
If CQI test need is confirmed, then move forward to further discussion on HST CQI test metric, test method and CQI test configurations.
Page 4~6 is for Information e.g. test metric.

## Slide 4: For information
  Simulation assumption :
  Scenario: Dmin=1000m, Ds=50m.
SNR definition: normalized SNR
CQI reporting interval: 5/10 ms

## Slide 5: For information
CQI test metric
In last meeting, three options were proposed:
  Option 1:Use TP2/TP1 with option 1 definition as the test metric to distinguish legacy and advanced UE.
    TP1: throughput performance with follow CQI during 1000m~1100m region in the SFN scenario channel model;
    TP2: throughput performance with follow CQI during 1000m~2000m region in the SFN scenario channel model.
  Option 2:The reported CQI values shall be in the range of +-1 of the reported median more than [90]% of the time.
  Option 3:The existing frequency non-selective fading test method can be considered for CQI reporting on high speed.
Other options are not precluded
If it is decided that new CQI tests are needed for SFN scenario, the options should be down selected.

## Slide 6: For information
Encourage companies to provide the analysis and evaluation results.