## Slide 1: WF on OTA requirement compliance range
NTT DOCOMO
3GPP TSG-RAN WG4 Meeting #81 R4-1610800
Reno, USA, 14 – 18 November, 2016

## Slide 2: Background
For OTA requirements, such as EIRP accuracy [1] and EVM [2], it was agreed that manufacturers declared the directions sets where each OTA requirement could be specified.
However, in general, these directions sets would be different because each requirement attributes different physical factors.
At this meeting, the contribution on OTA requirement compliance range for eAAS BS was submitted and discussed[3].
  It discusses the necessity of the common range where performance can meet for all requirements.
Following the discussion in eAAS evening adhoc, this WF is captured the agreements on declaration of common OTA requirement compliance coverage and open issues for following meetings.

## Slide 3: Way Forward
Followings are agreements in RAN4#81:
As mandatory, manufacturers need to declare a common peak directions set(s) (hereafter called “OTA compliance peak directions set” in this WF. Final naming is FFS). Any requirement specified at the peak direction is met in “OTA compliance peak directions set”.

## Slide 4: Way Forward
Followings are agreements in RAN4#81:
As mandatory, manufacturers need to declare a common direction ranges set(s) (hereafter called “OTA compliance coverage” in this WF. Final naming is FFS).
All OTA requirements must be met in the “OTA compliance coverage” (under the corresponding inherent conditions required for each requirement) with exception to the requirements that are specified at the peak direction or as a TRP.
In case a requirement that is not specified as peak direction or TRP but has a condition of a peak direction apply to it, then the peak direction must be within the “OTA compliance peak directions set” .
  “OTA compliance peak directions set” is a subset of “OTA compliance coverage”.

## Slide 5
Following is open issue need to be addressed:
Whether “OTA compliance coverage” for DL(TX) and “OTA compliance coverage” for UL(RX) should be aligned or not.
Definitions and names of “OTA compliance peak directions set” and “OTA compliance coverage” need to be agreed.
Companies encouraged to submit their view on which core RF requirements belong with each directions set for the next meeting.

## Slide 6: References
[1] TS 37.105 v.13.1.0 July 2016
[2] R4-168873, “WF on OTA EVM requirement for AAS”, NEC.
[3] R4-1609731, OTA requirements compliance range, NTT DOCOMO