## Slide 1: Way forward on remaining issues for Rel-13 multi-node testing
Source: Ericsson, Qualcomm, Nokia, Huawei, Verizon
[AT&T, T-Mobile USA]
Agenda item: 7.1.1
For: Approval
3GPP TSG-RAN WG4 Meeting #81 R4-1610950
Reno, NV, USA, 14-18 November, 2016

## Slide 2: Test scenario
Aggressor traffic type best effort vs victim traffic best effort
Aggressor traffic type best effort vs victim traffic VoIP
For best effort, UDP traffic [full buffer/finite traffic] in DL in both aggressor and victim link
For VoIP, the traffic will be bidirectional.
<No agreement>

## Slide 3: Test Scenario (Under discussion)
The purpose of the test when WiFi is the aggressor is to help 3GPP to validate LAA and enhancement of system performance; there will be no pass/fail criterial for WiFi (AGREED)
The above bullet is valid for existing WiFi systems only
Scenario | Victim system |  | Aggressor system |  |  |  | Traffic Type for both victim and aggressor
 | Victim device to be tested | Companion victim device | Aggressor device in baseline | Companion aggressor device | Aggressor device to be tested | Companion aggressor device | 
1 | Wi-Fi AP | Wi-Fi STA | Wi-Fi AP | Wi-Fi STA | LAA BS | LAA UE | Best effort
2 | Wi-Fi AP | Wi-Fi STA | Wi-Fi AP | Wi-Fi STA | LAA BS | LAA UE | Voice
3 | LAA BS | LAA UE | LAA BS | LAA UE | Wi-Fi AP | Wi-Fi STA | Best effort
4 | LAA BS | LAA UE | LAA BS | LAA UE | Wi-Fi AP | Wi-Fi STA | Voice

## Slide 4: Device parameter settings (Agreed)
The tests shall ensure repeatability and representative operational behavior.
The starting point of the configuration of both 802.11 and LAA equipment shall be based on the default settings.
In order to achieve the test objectives of repeatability and representative operational behavior, modifications to the default settings might or might not be needed
The above modifications, if needed, are FFS
Modifications compared to the defaults settings, if any, shall be documented

## Slide 5: Throughput Tests: Rx levels (current proposals)
Proposed RX levels in dBm
  -72+∆1 and -82-∆2 (R4-168545)
  -62+∆ and -82-∆ (R4-167653)
  -62 ±∆ and -82 ±∆ (R4-165830)
  -62 and -82 (R4-168405)
  -57dBm, -67dBm, -77dBm, -82dBm(R4-167941)
Agreement in red color:
  Only two levels, one below and one above LAA ED threshold [Agreed]
  [(1) -67dBm/20MHz; (2) -80dBm/20MHz] [Open for discussion]

## Slide 6: Throughput Tests: target operating point (current proposals)
SNR/SINR/SIR levels
  SINR=15dB (R4-168545)
  SNR=16dB (R4-167653)
  SIR=15dB (R4-165830)
  SIR=0dB (R4-167941)
  SINR = 0dB(R4-168405)
Proposals
  How many values to be selected are FFS.
  Exact value is also FFS
  SIR should be connected to RX signal levels between the AP and LAA BS

## Slide 7: Throughput Tests: pass fail criteria (current proposals)
Pass fail criteria
  Median of recorded throughput CDF (R4-168545)
  Mean of the recorded throughput CDF (R4-165830)
  Normalized best effort throughput and at {25%ile, 50%ile, 75%ile} (R4-167941)
  Mean of the recorded throughput CDF (R4-168405)
Only one pass/fail criteria is considered
  Median with 10% Accuracy for pass/fail criteria

## Slide 8: Outage test
Similar to throughput test
  Test setup
  Choice of devices
  RX levels
  Operating point
Traffic cases
  VoIP traffic in both links
Pass/fail criteria:
  MOS criteria: detail are FFS