## Slide 1: WF on BCS for CA_3A-28A
NTT DOCOMO, INC.
R4-1610988
3GPP TSG-RAN WG4 Meeting #81
Reno, NV, USA, 14 – 18 December 2016

## Slide 2: Background
2DL/2UL CA_3A-28A was proposed in the basket WI as below.
This CA configuration has no MSD issue and the TP (R4-167399) was approved in RAN4#80bis.
After this, however, it was identified that the existing BCS0 of CA_3A-28A has 15 and 20 MHz CBW in Band 28.
E-UTRA CA configuration / Bandwidth combination set |  |  |  |  |  |  |  |  |  | 
E-UTRA CA Configuration | Uplink CA configurations | E-UTRA Bands | 1.4 MHz | 3 MHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | Maximum aggregated bandwidth [MHz] | Bandwidth combination set
CA_3A-28A | CA_3A-28A | 3 |  |  | Yes | Yes | Yes | Yes | 30 | 0
 |  | 28 |  |  | Yes | Yes |  |  |  | 
E-UTRA CA configuration / Bandwidth combination set |  |  |  |  |  |  |  |  |  | 
E-UTRA CA Configuration | Uplink CA configurations (NOTE 4) | E-UTRA Bands | 1.4 MHz | 3 MHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | Maximum aggregated bandwidth [MHz] | Bandwidth combination set
CA_3A-28A | - | 3 |  |  | Yes | Yes | Yes | Yes | 40 | 0
 |  | 28 |  |  | Yes | Yes | Yes | Yes |  | 
 |  | 3 |  | Yes | Yes | Yes | Yes | Yes | 40 | 1
 |  | 28 |  |  | Yes | Yes | Yes | Yes |  | 
Table 5.6A.1-2: E-UTRA CA configurations and bandwidth combination sets defined for inter-band CA (two bands)

## Slide 3: Proposal to solve the inconsistency
To specify UL CA_3A-28A without a note as below and agree the big CR
In the next plenary, the original proposal in the WID will be modified to have consistency with the spec above.
Also, the corresponding TP will be approved in the next RAN4.
Table 5.6A.1-2: E-UTRA CA configurations and bandwidth combination sets defined for inter-band CA (two bands)
E-UTRA CA configuration / Bandwidth combination set |  |  |  |  |  |  |  |  |  | 
E-UTRA CA Configuration | Uplink CA configurations (NOTE 4) | E-UTRA Bands | 1.4 MHz | 3 MHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | Maximum aggregated bandwidth [MHz] | Bandwidth combination set
CA_3A-28A | CA_3A-28A | 3 |  |  | Yes | Yes | Yes | Yes | 40 | 0
 |  | 28 |  |  | Yes | Yes | Yes | Yes |  | 
 | - | 3 |  | Yes | Yes | Yes | Yes | Yes | 40 | 1
 |  | 28 |  |  | Yes | Yes | Yes | Yes |  |