## Slide 1: Way forward: further working assumptions and agreements on eLAA TX requirements
Ericsson, Skyworks
3GPP TSG-RAN WG4 Meeting #81
Reno, NV, USA, 14 – 18 December 2016
R4-1610990

## Slide 2: Scope of this document
This WF covers items not covered in the agreed R4-1610836

## Slide 3: Occupied bandwidth in Japanese regulation
Include a Japan-specific requirement on the occupied bandwidth applicable when the NS value relevant for Japan is indicated

## Slide 4: In-band emissions
The Rel-8 emission mask based on superposition of emissions from 1 RB transmissions received by the eNB
Working assumption: Qualcomm proposal (add masks) approximated, and with waveforms in accordance with the Ericsson proposal, e.g.
  Consider impact of IMD
Chart: Ericsson proposal (R4-1609568)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
 | -18 | -23 | -28 | -33 | -38 | -33 | -28 | -23 | -18
 | -21 | -26 | -31 | -36 | -41 | -36 | -31 | -26 | -21
 | -25 | -29 | -35 | -40 | -45 | -40 | -35 | -29 | -25
Chart: Qualcomm proposal (R4-1610197)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
 | -18 | -23 | -27 | -31 | -32 | -31 | -27 | -23 | -18
 | -21 | -26 | -30 | -33 | -34 | -33 | -30 | -26 | -21
 | -25 | -28 | -32 | -34 | -35 | -34 | -32 | -28 | -25
(20 MHz)
Relative emissions
for QPSK (1), 16QAM (2) and 64QAM (3)

## Slide 5: Background to general time mask
PUSCH transmissions by two different UEs
  End of PUSCH SF for UE1 and start of PUSCH SF for UE2
Shifting the trailing transient period (UE1) by T = [5] ms not to unduely increase idle time between PUSCH transmissions from different UEs contending for the channel and decrease risk of collisions

## Slide 6: General ON/OFF mask
Evaluate the feasibility of shifting the trailing transient period by 5 ms to start ramp-down later, OFF power starts 5 ms after the last symbol (ending symbol 13 or 14)

## Slide 7: Transmission templates
Agreement at RAN1#86
  The UE is not expected to start a new transmission subject to LBT earlier than 1 DFTS-OFDM symbol after the end of the previous transmission by the UE
LBT can only be made between subsequent PUSCH transmissions from the same UE if the ending symbol of the preceding subframe is 13
Evaluate the feasibility of shifting the transient period of the preceding subframe by [5] ms
OFF power requirement starts 5 ms after the start of the ending symbol

## Slide 8: Include U-NII3
From §15.407
(3) For the band 5.725-5.85 GHz, the maximum conducted output power over the frequency band of operation shall not exceed 1 W. In addition, the maximum power spectral density shall not exceed 30 dBm in any 500-kHz band. If transmitting antennas of directional gain greater than 6 dBi are used, both the maximum conducted output power and the maximum power spectral density shall be reduced by the amount in dB that the directional gain of the antenna exceeds 6 dBi.
(4) For transmitters operating in the 5.725-5.85 GHz band:
  (i) All emissions shall be limited to a level of −27 dBm/MHz at 75 MHz or more above or below the band edge increasing linearly to 10 dBm/MHz at 25 MHz above or below the band edge, and from 25 MHz above or below the band edge increasing linearly to a level of 15.6 dBm/MHz at 5 MHz above or below the band edge, and from 5 MHz above or below the band edge increasing linearly to a level of 27 dBm/MHz at the band edge.
Emissions requirements for 5725-5850 MHz shall be included in 36.101
A-MPR is not needed

## Slide 9: Band combinations
Consider Band 2 + Band 46 as an example for setting requirements for other combinations
  this combination has issues with harmonic mixing (impact on licensed band)
Companies to evaluate impact on licensed band of harmonic mixing