## Slide 1: Way forward on BS class for NR BS
NEC, Ericsson, ZTE, Huawei
3GPP TSG-RAN WG4 Meeting #82
Athens, Greece, 13th – 17th February, 2017
R4-1702357
Agenda item: 10.4.3.2
Document for: Approval

## Slide 2: Background
Agreements in [1]
  The deployment scenarios to which the BS classes relate will be described by means of a minimum distance (in 3D space) of UE to BS
Analysis of minimum distance for UTRA/E-UTRA BS
  Calculation of MCL for Local Area BS is described in [2, 3]
    … a minimal separation of 2 metres between UE and indoor BS is assumed. Free space path loss is defined in [4] as:
    Path loss [dB] = 38.25 + 20 log10(d [m])
    Taking into account 0dBi antenna gain for Local area BS and UE and a body loss of 1dB at the terminal, a MCL of 45.27 dB is obtained.
  From the description above
  Local Area BS: 2 m
  From MCL (70dB for WA BS and 53dB for MR BS)
  Wide Area BS: 35 m
  Medium Range BS: 5 m

## Slide 3: Agreements
NR BS classes for BS without antenna connectors are defined as indicated bellow:
  Wide Area Base Stations are characterised by requirements derived from Macro Cell scenarios with a BS to UE minimum distance along the ground equal to 35 m.
  Medium Range Base Stations are characterised by requirements derived from Micro Cell scenarios with a BS to UE minimum distance along the ground equal to 5 m.
  Local Area Base Stations are characterised by requirements derived from Pico Cell scenarios with a BS to UE minimum distance along the ground equal to 2 m.
NR BS classes for BS with antenna connectors are defined as indicated bellow:
  Wide Area Base Stations are characterised by requirements derived from Macro Cell scenarios with a BS to UE minimum coupling loss equal to 70 dB.
  Medium Range Base Stations are characterised by requirements derived from Micro Cell scenarios with a BS to UE minimum coupling loss equals to 53 dB
  Local Area Base Stations are characterised by requirements derived from Pico Cell scenarios with a BS to minimum coupling loss equal to 45 dB.
The following text is added together with any definition of BS classes:
  The deployment scenarios associated with and definitions of BS classes are exactly the same for BS both with and without connectors. An MCL of 70dB corresponds to a minimum distance of around 35m, 53dB to around 5m and 45dB to around 2m respectively for BS with connectors.
NR Home BS class is FFS.

## Slide 4: References
[1] R4-1700277, Way Forward on BS class description, Ericsson
[2] 3GPP TR 25.951 FDD Base Station (BS) classification
[3] 3GPP TR 25.952 TDD Base Station (BS) classification