## Slide 1: WF on new BS classes for NB-IoT
Ericsson, Nokia, Alcatel-Lucent Shanghai Bell, Huawei
3GPP TSG-RAN WG4 Meeting #82bis Spokane, WA, USA, 3 - 7 April, 2017
R4-1704047

## Slide 2: Background
Contributions on the following topics have been discussed in RAN4#82bis:
  BS RF requirements overview [1, 2].
  Needed simulations to set RF requirements and assumptions [3, 4].
References:
  [1] R4-1703536 Overview on NB-IoT small cells, Huawei
  [2] R4-1703010 NB-IoT small cell support: BS RF impacts, Ericsson
  [3] R4-1703009 NB-IoT small cell support coexistence studies,Ericsson
  [4] R4-1703011 NB-IoT small cell support: simulation assumptions for coexistence studies, Ericsson

## Slide 3: Background - agreements
No coexistence simulations needed with NB-IoT standalone with E-UTRA, UTRA and GSM:
  Covered by NB-IoT macro BS coexistence simulations results.
No coexistence simulations needed for In-band and guard band:
  BS shall be compliant with E-UTRA requirement.
  Covered by E-UTRA coexistence simulations outcome then.

## Slide 4: Way forward
Micro and pico would be first considered.
Coexistence simulations (standalone NB-IoT vs standalone NB-IoT) are needed to set BS RF requirements, e.g. REFSENS, interferer level, …
Following simulations should be considered as a baseline. Further down-selection could be decided by next RAN4#83 meeting if motivated.

## Slide 5: List of needed simulations
Case | Aggressor | Victim | Simulated link | Statistics | Target BS RF requirement
M1 | Micro | Micro | UL | SNR loss | Reference sensitivity
 |  |  |  | SNR loss + Interferer levels at victim BS | ACS In-band blocking
M2 | Micro | Macro | UL | SNR loss | Reference sensitivity
M3 | Macro | Micro | UL | SNR loss + Interferer levels at victim BS | ACS In-band blocking
Case | Aggressor | Victim | Simulated link | Statistics | Target BS RF requirement
P1 | Pico | Pico | UL | SNR loss | Reference sensitivity
 |  |  |  | SNR loss + Interferer levels at victim BS | ACS In-band blocking
P2 | Pico | Macro | UL | SNR loss | Reference sensitivity
P3 | Macro | Pico | UL | SNR loss + Interferer levels at victim BS | ACS In-band blocking

## Slide 6: Open issues
To be further investigated and agreed at next RAN4#83 meeting:
  Deployment scenarios
    R4-1703009 could be used as starting point.
  What type of deployment should be used for macro BS in simulations?
    Macro suburban (ISD=1723m)?
    Macro urban (ISD=500m)?
    Both?
  Simulations assumptions:
    R4-1703011 could be used as starting point (should be 19 sites instead of 7).
  Is it needed to check ACLR by running following coexistence simulations?
Case | Aggressor | Victim | Simulated link | Statistics | Target BS RF requirement
M4 | Micro | Micro | DL | SNR loss | ACLR
M5 | Micro | Macro | DL | SNR loss | ACLR
Case | Aggressor | Victim | Simulated link | Statistics | Target BS RF requirement
M4 | Pico | Pico | DL | SNR loss | ACLR
M5 | Pico | Macro | DL | SNR loss | ACLR