## Slide 1: WF on 3.3-4.2 GHz and 4.4-4.99 GHz NR spectrum
NTT DOCOMO, INC., Intel, Qualcomm, Qorvo, Skyworks, Ericsson
3GPP TSG-RAN WG4 #82bis Meeting Spokane, WA, USA, 3 - 7 April, 2017
R4-1704410

## Slide 2: Background on 3.3-4.2 GHz (1)
Based on online [1-7] and offline discussions, there were two proposals to specify the band in the range of 3.3-4.2 GHz.
  Proposal 1: To specify two different bands below with a note indicating that “A UE supporting Band X shall also support Band Y and vice versa”.
    Band X: 3.3-3.8 GHz
    Band Y: 3.6-4.2 GHz *No additional switch loss is assumed.
  Proposal 2: To specify 3.3-4.2 GHz as a single band.
 | Pros | Cons
Proposal 1 | Allow two PAs implementation | UL contiguous CA over 200MHz including 3.6-3.8 GHz is restricted Double RAN4 works (e.g., B1+BX and B1 +BY)
Proposal 2 | No spec restriction Simpler spec | May force UE to implement one PA
Band X
Band Y
Band Z
3.3
3.8
3.6
4.2
4.2
3.3

## Slide 3: Background on 3.3-4.2 GHz (2)
In the absence of regulatory limits for the mobile service in the frequency ranges considered, the need for RAN4 studies of compatibility with the airplane altimeter in 4.2-4.4 GHz was raised [7].
  In Japan a study funded by MIC has been carried out for LTE-Advanced in 3.6-4.2GHz, report still to be published

## Slide 4: WF on 3.3-4.2 GHz
One of options below should be selected considering their pros/cons in RAN4#83.
  Option 1: Proposal 1
  Option 2: Proposal 2
  Option 3: Proposal 1 & 2 (which means specifying three different bands and the NW needs MFBI) RAN4 agrees that compared to a device only supporting 3.3-3.8 GHz, there shall be no additional losses in the TRx path within 3.3-3.8 GHz for a device supporting 3.3-4.2 GHz.
Companies are encouraged to provide technical aspects of their preferred proposal, including but not limited to efficiency and gain flatness.
How to treat the altimeter protection should be studied further
  If necessity of the study in 3GPP is identified, a possible way is to perform coexistence studies with the radio altimeter service with parameters based on the ITU-R Rec. 2059-0
Requirements near 4.2 GHz subject to outcome of coexistence study if necessary

## Slide 5: Background on 4.4-4.99 GHz
There was a proposal to specify 4.4-4.99 GHz as a single band [8, 9].
In the absence of regulatory limits for the mobile service in the frequency ranges considered, the need for RAN4 studies of compatibility with the airplane altimeter in 4.2-4.4 GHz was raised [7].
  In Japan a study funded by MIC has been carried out for LTE-Advanced in 4.4-4.9GHz, report still to be published

## Slide 6: WF on 4.4-4.99 GHz
To specify 4.4-4.99 GHz as a single band.
How to treat the altimeter protection should be studied further
  If necessity of the study in 3GPP is identified, a possible way is to perform coexistence studies with the radio altimeter service with parameters based on the ITU-R Rec. 2059-0
Requirements near 4.4 GHz subject to outcome of coexistence study if necessary

## Slide 7: References
3.3-4.2 GHz
  [1] R4-1702800 Consideration on 3.5GHz band definition Samsung
  [2] R4-1703101 3.5GHz Band Arrangement Qualcomm Incorporated
  [3] R4-1703218 Further consideration on defining NR spectrum for sub-6GHz Intel Corporation, Qorvo
  [4] R4-1703337 Discussion on feasibility of NR band in 3.3-4.2GHz CMCC
  [5] R4-1703436 Band definition of frequency range of 3.3-4.2GHz NTT DOCOMO INC.
  [6] R4-1703557 General considerations on NR bands for 3.2-4.2 and 4.4-4.99GHz Nokia, Alcatel-Lucent Shanghai Bell
  [7] R4-1703571 Discussion on Implementation Aspects of 3.5GHz and 4.5GHz NR Frequency Ranges Skyworks Solutions Inc. Ericsson
4.4-4.99 GHz
  [8] R4-1703573 Proposal on NR band covering 4.4-4.99GHz DOCOMO Communications Lab.
  [9] R4-1702866 Proposals on how to specify 4.5 GHz spectra KDDI Corporation