## Slide 1
Way on UE Tx EVM for mmW
Qualcomm, ?
3GPP TSG-RAN WG4 #84
Berlin, Germany, 21st – 25th August, 2017
Agenda: 9.4.3.1.2
R4-1708813

## Slide 2: Background
mmW ACLR requirement is -17 dBc as opposed to -30 dBc for LTE
LTE TX EVM is anticipated to be un-necessary tight for system needs for low order modulations
Pi/2-BPSK EVM is not known since discussion for MCS vs BS SNR is not settled
  Normally, SNR is discussed in RAN1 with MCS work and possibly specified in RAN4 demodulation work
RAN4 work for mmW maximum output power and MPR needs information and agreement on Tx EVM
To agree TxEVM, RAN4 needs understanding on BS RX SNR for each modulation

## Slide 3: Background
UE Tx EVM requirement should be such that UE Tx performance does not impact too much negatively to the link throughput
For mmW UE, current LTE EVM requiements will limit output power
Parameters to consider when defining Tx EVM for UE:
  BS Rx SNR for different channel conditions
  System interference with different loads
  UE implementation feasibility

## Slide 4: Way Forward
To accelerate RAN4 work, companies are encouraged to provide needed BS RX SNR at mmW especially for modulations:
  Pi/2-BPSK
  QPSK
  16 QAM
Companies are further encouraged to provide input on system interference at mmW and analysis on feasible UE TX EVM with consideration of suitable contribution of UE Tx EVM to system interference