## Slide 1: Way Forward on MPR and A-MPR for PC2 with UL CA in Band 41
Qualcomm Incorporated, Nokia,
R4-1708816

## Slide 2: MPR for PC2 with UL CA bandwidth class C Contiguous allocations
Proposals for MPR in [1] and [2]. For contiguous allocations, the following compromise is proposed as way forward
Modulation | CA bandwidth Class C / Smallest Component Carrier Transmission Bandwidth Configuration |  |  |  | MPR (dB)
 | 25 RB | 50 RB | 75 RB | 100 RB | 
QPSK | > 6 and ≤ 25 | > 6 and ≤ 50 | > 6 and ≤ 75 | > 6 and ≤ 100 | ≤ 1
QPSK | > 25 | > 50 | > 75 | > 100 | ≤ 2
16 QAM | ≤ 6 | ≤ 8 | ≤ 16 | ≤ 18 | ≤ 1.5
16 QAM | > 6 and ≤ 25 | > 8 and ≤ 50 | > 16 and ≤ 75 | > 18 and ≤ 100 | ≤ 2
16 QAM | > 25 | > 50 | > 75 | > 100 | ≤ 3
64 QAM | ≤ 8 and allocation wholly contained within a single CC | ≤ 12 and allocation wholly contained within a single CC | ≤ 16 and allocation wholly contained within a single CC | ≤ 18 and allocation wholly contained within a single CC | ≤ 2
64 QAM | > 8 or allocation extends across two CC's | > 12 or allocation extends across two CC's | > 16 or allocation extends across two CC's | > 18 or allocation extends across two CC's | ≤ 3
256 QAM | FFS |  |  |  | FFS
Table 6.2.3A-1: Maximum Power Reduction (MPR) for Power Class 2

## Slide 3: MPR for PC2 with UL CA bandwidth class C Non-contiguous allocations
Proposal in [1] is way forward

## Slide 4: A-MPR for PC2 under CA_NS_04 Contiguous allocations
Proposal in [3] is way forward.
For lower frequency channels, the following table is provided. For upper frequency channels, the MPR can be reused. The cutoff between lower frequency and upper frequency is FFS.

## Slide 5: A-MPR for PC2 under CA_NS_04 Non-contiguous allocations
Proposal in [3] is way forward.
For lower frequency channels and upper frequency channels, the formulations are provided below. The cutoff between lower frequency and upper frequency is FFS.
For lower frequency channels,
MA = 13.0, 0≤ A < 0.05
= 15.33 – 46.67A, 0.05≤ A < 0.20
= -7.0 – 5.0A, 0.20≤ A < 0.50
= 4.5, 0.50 ≤ A ≤ 1.
For upper frequency channels,
MA = 8.2, 0.00 ≤ A < 0.04
= 9.8 – 40.0A, 0.04≤ A < 0.075
= 8.0 – 16.0A, 0.075 ≤ A < 0.25
= 4.83 – 3.33A, 0.25 ≤ A < 0.40
= 3.83 – 0.83A, 0.075 ≤ A ≤ 0.25

## Slide 6: References
[1] R4-1708599, “MPR for Power Class 2 with UL CA in Band 41,” Qualcomm Incorporated
[2] R4-1707594, “Power class 2 UL CA MPR for contiguous allocations,” Nokia
[3] R4-1708600, “CA_NS_04 A-MPR for Power Class 2 with UL CA in Band 41,” Qualcomm Incorporated