## Slide 1: WF on Further clarification of wideband operation
LG Electronics, Media TeK, Huawei, Nokia, ZTE
R4-1708849
3GPP TSG-RAN WG4 #84 Meeting
Berlin, Germany, August 21st -25th, 2017
Agenda: 9.3.1

## Slide 2: Background (1)
LS from RAN1
  R1-1706615 LS on Wideband Operating Options
WF in RAN4 NR AH #2
  R4-1706927 WF on Channel Bandwidth, Qualcomm Incorporated
Contributions in RAN4 #84
  R4-1708170 Discussion on UE RF requirements on wideband operation ZTE
  R4-1708188 Further consideration on transparency in wideband operation ZTE
  R4-1708135 Discussion on wide band operation Huawei
  R4-1708164 Consideration on wideband operation for NR UE LGE
  R4-1707090 Clarification on wideband operation Samsung
In RAN4 #84 meeting, RAN4 has been discussed in terms of the related UE RF requirements, UE capability and gNB impact.

## Slide 3
Definition of wideband operation
  RAN1 Agreements of Wideband operation (R1-1706615)
    A gNB can operate simultaneously as wideband CC for some UEs and as a set of intra-band contiguous CCs with CA for other UEs.
Background (2)

## Slide 4
Definition of wideband operation
  RAN4 can specify wideband operation requirements for these cases with the wideband aggregated Channel bandwidths in rel-15.
    For sub-6GHz:
      Aggregated CBW > 50MHz (SCS 15KHz) or 100MHz(SCS 30kHz/60kHz)
    For mmWave : Two options will be further discussed in next RAN4 meeting
      Option1: Aggregated CBW > 200MHz (SCS 60kHz) or 200MHz (SCS 120kHz)
      Option2: Aggregated CBW > 200MHz (SCS 60kHz) or 400MHz (SCS 120kHz)
Way Forward (1)

## Slide 5
RF requirements for wideband operation
  Q1) What RF requirement for UE and BS is specified for wideband operation?
  A1) Intra-band contiguous CA requirements are a starting point for UE wideband requirements (pending agreements on spectrum utilization etc.).
  Q2) Are the RF requirements set based on the single channel bandwidth ?
  A2) The RF requirements could potentially be different compared to single channel bandwidth(X) and aggregated wideband (Y) operation (Y>X). Detailed RF requirements are FFS.
  Q3) Is it based on zero guard band or is it based on a particular component carrier spacing?
  A3) Zero GB will be considered as a starting point. Also, non-zero GB is not precluded based on channel raster decision.
Way Forward (2)

## Slide 6
UE capability for wideband operation
  Following UE capabilities should be signaled at least
    Supporting the simultaneous multiple numerology (Data/Data)
    Maximum Channel BW
    Information on combinations/number of aggregated CCs
      FFS how many different permutations of CA combinations should be signaled
    Supported RF Bands and corresponding parameters for wideband operation
      E.g.) SCS for multiple numerology (Data/Data), detail parameters are FFS.
  *Additional UE capability signals are not precluded.
Way Forward (3)