## Slide 1: WF on band numbering
NTT DOCOMO
3GPP TSG- RAN Working Group 4 (Radio) meeting #84 R4-1708966
Berlin, Germany, 21-25 August 2017

## Slide 2: Back ground
At the RAN4 June AH meeting, the following agreements were made for band numbering [R4-1706892]
  For NR in LTE “refarming” bands, reuse LTE band numbers for NR
    Use prefix “n” to differentiate from LTE bands
    Ex. LTE Band 1  NR Band “n1”
  New bands for NR are assigned band numbers on a “first come first served” basis in reserved ranges regardless of duplex mode or RAT
    Reserved range is 65-256 for new LTE (FDD) and new NR sub6 bands, 257-512 for NR mmW bands
    New LTE only TDD band can use band number from existing LTE TDD numbering space until all numbers up to 63 are used and after that from 65-256 space.
  For both re-farming LTE bands and new NR bands, duplex mode should be assigned and described in band defining table (e.g. in 38.101)
    TDD for unpaired bands and FDD for paired bands
      FFS: flexible duplexing for paired bands
    If multiple duplexing modes are allowed in a specific frequency range, separate bands will be introduced with each duplexing mode
  Remaining issues for RAN4 #84
    How to represent LTE-NR DC combination

## Slide 3: Proposal for NR bands
The prefix “n” is used for any NR bands
The following numbers are assigned to each of the new NR bands:
  NR range 1:
  NR range 2:
 | UL | DL | Duplexing mode
n77 | 3.3 - 4.2 GHz | 3.3 - 4.2 GHz | TDD
n78 | 3.3 - 3.8 GHz | 3.3 - 3.8 GHz | TDD
n79 | 4.4 - 5.0 GHz | 4.4 - 5.0 GHz | TDD
n80 | 1710 - 1785 MHz | N/A | SUL
n81 | 880 - 915 MHz | N/A | SUL
n82 | 832 - 862 MHz | N/A | SUL
n83 | 703 - 748 MHz | N/A | SUL
 | UL | DL | Duplexing mode
n257 | 26.5 –29.5 GHz | 26.5 –29.5 GHz | TDD
n258 | 24.25 – 27.5 GHz | 24.25 – 27.5 GHz | TDD
n259 | 31.8 – 33.4 GHz | 31.8 – 33.4 GHz | TDD
n260 | [37 – 43.5 GHz] | [37 – 43.5 GHz] | TDD

## Slide 4: Proposal for NR DC/CA representation
For non NR-LTE coexistence bands, the following notion is used:
  Note: The following band combination is just for example.
FFS: CA bandwidth class (postfix of the bands) for NR
  Ex. How to handle the single carrier operation with larger than 100PRBs
  Ex. How to handle different maximum bandwidth for each frequency range
FFS: How to handle BCS for NR
  Ex. Reuse exiting BCS concept or adopt simplified BCS concept
Representation | Functionality
CA_n77-n78 | NR CA of band n77 and band n78
DC_1-2_n77 | NR-LTE DC with LTE CA of band 1 and band 2 and NR band n77
DC_1-2_n77-n78 | NR-LTE DC with LTE CA of band 1 and band 2 and NR CA of band n77 and band n78

## Slide 5: Proposal for SUL and NR-LTE coexistence representation
For SUL and LTE-NR coexistence bands:
  Note: The following band combination is just for example.
Any possible new additional combinations not captured by this way forward will be discussed, if needed
Representation | Functionality
SUL_n78-n81 | Band combination of NR band n78 and band n81(SUL) for NR operation including but not limited to NR-LTE coexistence with UL sharing
DC_3-SUL_n78-n80 | LTE-NR DC between LTE Band 3, and NR bands n80 (SUL) and n78 including NR-LTE coexistence with UL sharing