## Slide 1: Summary of NR progress in RAN4
CMCC
3GPP TSG-RAN WG5 Meeting #76 R5-173905 Berlin, Germany, 21 - 25 August 2017

## Slide 2
Overall progress
1
General RF
2
Tx requirement
3
Rx requirement
4
RRM
5
Testability
6
RAN5 affection
7

## Slide 3
Overall time plan
The overall RAN4 discussion for NR are divided into RF and RRM, at this moment demod has not been involved.
From the RF time plan, RAN4 will complete the sub-6GHz RF spec by the end of this year. But for mmW, it is not clear what’s the completion status by Dec 2017, but the final target completion date is mid 2018.
For RRM, it is targeted to complete NSA this year, then SA specific requirements by June 2018.
Notes: Reference: R4-1703469 Workplan for NR UE and BS RF

## Slide 4
RAN4 spec structure is important for RAN5 to plan the testing specs.
From 3GPP website it seems there are four sections for RF/demod, i.e. 38.101, 38.101-1, 38.101-2, 38.101-3, but from the discussion in June NR AH, it seems the spec structures have not been decided in RAN4.
Below are some options, different specs for sub-6GHz and mmW are expected.
NR 38.101 structure
Notes: Reference: R4-1706941 Summary of discussions of spec structure 38.101

## Slide 5
NR 38.133 structure
At this moment the structure of TS38.133 is similar to 36.133.
It seems conducted test and OTA test are all included in this spec. How to merge them is not clear.

## Slide 6
Overall progress
1
General RF
2
Tx requirement
3
Rx requirement
4
RRM
5
Testability
6
RAN5 affection
7

## Slide 7
NR frequency ranges
  For the sub-6GHz refarming bands, Band 1,3,7,8,20,28,41,66,70 are introduced for NR based on operator refarming plan.
  For the sub-6GHz new bands, 3.3-4.2GHz and 4.4-4.99GHz are the most popular frequencies which may be divided into several new bands based on the real deploy plans in different areas;
  For mmW, 24.25-29.5GHz, 31.8-33.4GHz and 37-40GHz are the potential deploy frequencies. Most likely these frequencies will be used for NSA deploy scenario and worked with LTE.
NR bands include legacy refarming bands and new bands. The new bands include sub-6GHz NR frequencies and mmW frequencies.

## Slide 8
Band numbering has been decided
NR bands include refarming bands and new bands, the numbering rule are different.
For NR in LTE “refarming” bands, reuse LTE band numbers for NR
  Use prefix “n” to differentiate from LTE bands
  Ex. LTE Band 1  NR Band “n1”
New bands for NR are assigned band numbers on a “first come first served” basis in reserved ranges regardless of duplex mode or RAT
  Reserved range is 65-256 for new LTE (FDD) and new NR sub6 bands, 257-512 for NR mmW bands
  New LTE only TDD band can use band number from existing LTE TDD numbering space until all numbers up to 63 are used and after that from 65-256 space.
For both re-farming LTE bands and new NR bands, duplex mode should be assigned and described in band defining table (e.g. in 38.101)
  TDD for unpaired bands and FDD for paired bands
  If multiple duplexing modes are allowed in a specific frequency range, separate bands will be introduced with each duplexing mode
Notes: Reference: R4-1706892 WF on NR band numbering

## Slide 9
Band Combination with LTE
Up to now, more than 15 NR bands are introduced, and more than 65 LTE 1CC + NR 1CC combinations are introduced. The number will increase when higher number of CCs and more combinations come. Similar situation as CA but even complex.
  LTE 1CC + one NR
  LTE 2DL/1UL + one NR
  LTE 3DL/1UL + one NR
  LTE 4DL/1UL + one NR
  LTE 5DL/1UL + one NR
  Intra-band NR CA (mDL/1UL)
  inter-band NR CA (nDL/1UL)
Rule:
When xDL/1UL + NR band is proposed, specifications for the LTE CA configuration of xDL/1UL shall be completed in advance.
In NSA mode, DC will be used to connect LTE and NR network simultaneously. Hence, UE need to support many LTE band + NR band combinations based on operator deploy scenarios.
Notes: Reference: R4-1704406 Handling NR band and band combination in Rel15 WI; R4-1706048 Further consideration for NR band and band combination in Rel15 WI

## Slide 10
SUL and UL sharing band
NR is discussing two new concept, SUL and UL sharing.
  SUL band is introduced in RAN1 to work with NR high freq bands to overcome the UL/DL coverage imbalance. The band definition has been agreed in RAN4 to specify SUL bands.
  UL sharing means NR could share a legacy UL band with LTE by FDD mode or TDD mode. The details are still under discussion in RAN1.
Notes: Reference: R4-1706967 Reply LS on support SUL in NR

## Slide 11
Sub-Carrier Spacing
Sub-Carrier Spacing (SCS) is different from LTE.
In LTE only 15kHz is used, but NR has introduced 15kHz, 30kHz, 60kHz and 120kHz for different frequency ranges and different use cases.
Larger SCS can support larger BW.

## Slide 12
BW definition
BW definition for NR is different from LTE. UE can support different max CBW in DL and UL. UE can operate with different UL and DL bandwidth. RAN4 will further discuss the related UE capability indication.
The maximum BW will be different for different bands and subcarrier spacing.
  For the refarming LTE bands, the maximum BWs are extended to beyond 20MHz, such as 60MHz for B41.
  For the new sub-6GHz bands the maximum BW is 100MHz for large subcarrier spacing.
  For mmW, the maximum BW will become 400MHz for 120KHz subcarrier spacing.
Notes: Reference: R4-1706979 WF on band specific UE channel bandwidth

## Slide 13
Spectrum Utilization
Spectrum utilization relates to how many RBs could be used in certain BW.
In LTE, 100RBs can be used for 20MHz and the spectrum utilization efficiency is 90%.
For NR, one RB still include 12 subcarriers, but due to four SCS exist in NR, the frequency per RB occupy will be different which lead to different RB numbers for one BW.
Generally speaking, the spectrum utilization efficiency for NR is higher than LTE, but not equal for different BW and SCS combinations.
Notes: Reference: R4-1706929 WF on Spectrum Utilization

## Slide 14
Channel Raster
The channel raster for LTE is 100 kHz for all bands, which means that the carrier centre frequency must be an integer multiple of 100 kHz.
For NR, there are two different channel raster, one is 100kHz raster, the other is RB based raster.
For sub-6GHz
  NR Bands should have the same raster for both UL and DL (for both UL and DL 100kHz or RB based raster is used)
  Channel raster could be different for different bands.
  Only a single raster should be defined per band.
For mmW
  Channel raster for frequency range 2 is based on the [RB size - 720kHz]
Notes: Reference: R4-1706975 WF on RF channel raster for sub6GHz and mmWave bands

## Slide 15
Overall progress
1
General RF
2
Tx requirement
3
Rx requirement
4
RRM
5
Testability
6
RAN5 affection
7

## Slide 16
UE assumption
For sub-6Hz, UE could support 1Tx antenna or 2Tx antennas, and support 2Rx antennas or 4 antennas.
  Requirements and test methods are similar to LTE.
For mmW, UE will support panel antennas and use beamforming to overcome large path loss. Due to small size, the RF connector will disappear.
  Requirements will be OTA based, like TRP and EIRP, rather than traditional conducted requirements.

## Slide 17
Power class
For sub-6Hz, UE power class include 23dBm and 26dBm.
  The relation to 1Tx and 2Tx are not clear at the moment, may include 1Tx 23dBm, 1Tx 26dBm, 2Tx 23dBm, 2Tx 26dBm. RAN4 needs further discussion.
For mmW, UE power class is based on EIRP. Maximum allowed TRP may also be specified. But there are still some open issues.
  Reference RF architecture is FFS.
  Whether multiple power classes should be defined in Rel15 is FFS.
  How to define the maximum TRP limit and whether this limit varies for different power classes are FFS.

## Slide 18
MPR/AMPR
MPR evaluation related to many conditions. For sub-6GHz, the assumptions have been agreed. For mmW not much detailed analysis has been done, mostly reuse sub-6GHz assumptions.
AMPR has not been started.
  MPR evaluation related conditions:
  Subcarrier spacing
  Channel bandwidth
  Spectrum utilization
  Tx maximum output power
  EVM requirement for each modulation order
  In-band emission / Carrier leakage
  Occupied bandwidth
  SEM requirements
  UE ACLR value
  General spurious
  Waveform

## Slide 19
EVM
EVM is related to waveform, NR use DFT-OFDM and CP-OFDM for UL rather than SC-OFDM, the EVM value may need to be re-evaluated.
  Most likely the EVM values will be reused for sub-6GHz.
  For mmW, there is no reference, but for MPR evaluation purpose uses the sub-6GHz values.
Modulation | EVM
Pi/2 BPSK | FFS%
QPSK | 17.5%
16QAM | 12.5%
64QAM | 8%
256QAM | 3.5%

## Slide 20
ACLR
ACLR definition is similar to LTE, with only one difference which is the measured BW becomes equal to the channel BW.
  In LTE, when the channel BW is 20MHz the ACLR measured BW is 18MHz not 20MHz.
  In NR, this means there will be 0 guard frequency and more stringent requirement.
  The ACLR value for sub-6GHz is equal to the LTE requirements at the moment for simulation purpose. The ACLR for mmW is less stringent due to not much system exist in such high frequency.
Notes: Reference: R4-1706613 Proposed ACLRs definition for NR UE Bellow 6GHz

## Slide 21
ON-OFF time mask
ON-OFF time mask has been discussed. The transient period is less dependent on bandwidth and subcarrier spacing but dependent on carrier frequency and UE architecture.
  For frequencies below 6 GHz, UE transient period for NR is 10 µsec.
  For frequencies above 24 GHz, UE transient period for NR is 5 µsec.
Notes: Reference: R4-1706940 LS Reply on transient period for NR

## Slide 22
SEM
The sub-6GHz value has been decided.
mmW is FFS.
Notes: Reference: R4-1706692 NR Sub-6 GHz SEM

## Slide 23
Spurious Emission
Spurious emission for sub-6GHz is clear, only extend the frequency range with -30dBm requirement.
For mmW, the requirement is not clear due to not much existing regulation requirements to refer to. RAN4 use FCC requirements and ITU-R emission limits as the baseline, i.e. -13dBm and -30dBm.
Notes: R7-1706938 WF on spurious emission for NR UE;
R4-1706980 WF on MPR evaluation assumption

## Slide 24
Inband Emission
Reuse LTE requirements for sub-6GHz for MPR evaluation purpose.
For mmW, not much discussion in RAN4. For MPR evaluation purpose, reuse LTE requirements.
Notes: R4-1706708 UE in-band emission requirement
R4-1706693 NR Sub-6 GHz In-band emission requirement

## Slide 25
Overall progress
1
General RF
2
Tx requirement
3
Rx requirement
4
RRM
5
Testability
6
RAN5 affection
7

## Slide 26
General
Receiver test requirements have not been discussed much up to now as much information need to be defined in RAN1 first, such as reference signal configuration etc.
About receiver sensitivity, MSD is discussed which is caused by harmonics and intermodulation products under LTE-NR co-existance scenario.
The ACS under sub-6GHz is initially agreed as below.

## Slide 27
Overall progress
1
General RF
2
Tx requirement
3
Rx requirement
4
RRM
5
Testability
6
RAN5 affection
7

## Slide 28
Measurement: RSRP/RSRQ/SINR
  RSRP: Up to now following aspects have been agreed.
  The RSRP and CSI-RSRP definition should include Rx beamforming gain for OTA
  For conducted, the reference point for definition can be antenna connectors.
RSRP: Following aspects are still under discussion.
  whether the definition should be differentiated across frequency ranges
  whether to include averaging in time domain in the definition:
  whether RSRP definition should be per SS block, per beam, or per cell. Up to now there are not much discussion about beam measurement, which need conclusion from RAN1.
  whether CSI-RSRP definition should be per cell or per beam
  RSRQ and SINR are used to evaluate the signal quality.

## Slide 29
Measurement: Intra/Inter freq
Difference 1: Reference signal for measurement is different.
  In LTE the CRS is used for RSRP/RSRQ/SINR measurement;
  In NR there is no CRS anymore, SS blocks and CSI-RS are used for measurement. The SS block can be configured flexibly in the freq domain.
Difference 2: Even intra freq may also need measurement GAP.
  In LTE the intra freq means the center of current cell and target cell are the same. Then the RRM measurement can always be done based on the center freq (6PRB).
  In NR, whether measurement gap is needed depend on the SS block location of current and target cell, rather than whether the two cells have the same center frequency.
    if the current cell and target cell SS block are not at the same freq, then the GAP is needed.
    if SS block at the same frequency, then UE can perform RRM measurement without gap assisted, even if they have different center frequencies.
Figure 1 measurement gap assisted scenario
Figure 2 without measurement gap assisted scenario
Notes: R4-1706717 Discussion on definitions of intra and inter-frequency measurements

## Slide 30
Simulation Assumption
  System level and Link level simulation assumptions have been agreed.
  System level simulation is used to evaluate
  Number of SS block beams to be detected
  Number of cells to be detected
  Mobility performance
  Link level simulation is used to evaluate
  RLM (in-sync and out-of-sync)
  Cell detection
  Beam identification
  Measurements for mobility and beam management (e.g., number of samples, measurement period, measurement accuracy etc.)
  Basic SI reading (PBCH acquisition)
  Any additional link study if needed for SA specifically

## Slide 31
NSA affection to LTE RRM
  In NSA scenario, DC is used. Some of LTE RRM requirements are affected by NR.
  Not affected sections:
    RRC IDLE state mobility -> No DC exist at this period
    RRC connected state mobility ->Follow existing LTE requirements
    RRC connection mobility control
      RRC re-establishment -> Pure LTE behavior
      Random access ->Defined in 38.133, not affect 36.133
      RRC connection release with redirection ->Pure LTE behavior
    Timing and Signaling
      Transmit timing & Timing advance & RLM ->Defined in 38.133, not affect 36.133
  Affected sections:
    Timing and Signaling
      Interruption with DC ->LTE PSCell addition/release requirements as baseline
    Measurement procedures
      Measurement gap pattern, inter-RAT NR measurement, measurement capability will be introduced in 36.133
      Measurement accuracy, report mapping for NR reference signals will be introduced in 36.133
Notes: R4-1706722 Expected RRM requirements for NSA in TS36.133

## Slide 32
Overall progress
1
General RF
2
Tx requirement
3
Rx requirement
4
RRM
5
Testability
6
RAN5 affection
7

## Slide 33
General
  RAN4 has set up a Study Item to research test methods for mmW RF/RRM tests. The study item target completion date is the end of this year and the output will be captured in TR38.810.
  The baseline test method considered now is far field OTA test. Some other test methods like Compact Antenna Test Range and Near Field test have also been discussed but at the first stage only consider Far Field Test method.
  Based on the observation, the OTA test method definition for mmW RF/RRM is quite slow, up to now no clear picture of how mmW UE will control its beam, how to define the corresponding requirements and how to test them.

## Slide 34
Channel Model for mmW
  Channel model is needed for RRM and demod tests.
  In RAN1, TR38.900 and TR38.901 there are some channel models used for mmW simulation purpose, but they are too complicate for RAN4 to test in OTA environment. Some of these channel models need to be simplified by RAN4.
Parameter | Units | UMi LOS | UMi NLOS | UMi O2I | UMa LOS | UMa NLOS | UMa O2I | IO LOS | IO NLOS
Applicability to mmWave |  |  |  |  |  |  |  |  | 
BS antenna height | m | 10 | 10 | 10 | 25 | 25 | 25 | 3 | 3
DUT speed | km/h | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3
Min. BS-DUT distance | m | 10 | 10 | 10 | 35 | 35 | 35 | 0 | 0
Delay scaling parameter r |  | 3 | 2.1 | 2.2 | 2.5 | 2.3 | 2.2 | 3.6 | 3
Cluster shadowing zeta | dB | 3 | 3 | 4 | 3 | 3 | 4 | 3 | 3
Cluster mean DS (norm) |  | 0.1076 | 0.1156 | 0.2178 | 0.1594 | 0.1432 | 0.2178 | 0.166 | 0.0969
Cluster mean AoA spread | deg | 1.2254 | 1.2482 | 1.4997 | 1.4997 | 0.8357 | 1.4997 | 1.4191 | 1.4191
Table 1: Selected parameters of fading scenarios from 38.901 for fc=39 GHz
Test case | Propagation condition | Num emulated cells
Cell re-selection | AWGN | 2
Handover | AWGN | 2
RRC re-establishment | AWGN | 2
Random access | AWGN | 1
Transmit timing | AWGN | 1
Timing advance | AWGN | 1
RLM | Fading, AWGN | 1
DC interruption | AWGN | 2
Event triggered measurement reporting | Fading | 2
Monitoring of multiple layers | Fading | 3
Positioning | Fading | 3
CA measurements | Fading, AWGN | 3, 4, 5
DC measurements | Fading | 2, 4
LTE RRM test environments
Notes: R4-1706514 On propagation model parameters for RRM and demodulation

## Slide 35
Test Interface for mmW
  UE test interface definition is very important for OTA test design, if the test system cannot control UE then test will be impossible.
  Some discussions happened during the NR AH meeting at high level, RAN5 may need to be involved in the test interface design at early stage.
Notes: R4-1706510 On test interface parameters

## Slide 36
Overall progress
1
General RF
2
Tx requirement
3
Rx requirement
4
RRM
5
Testability
6
RAN5 affection
7

## Slide 37
Observations
  Observation 1:
  Initially RAN5 discussed the time plan for NSA and SA options and conclude that the SA and NSA will start together. From RAN4 discussion it can be seen that there is no difference among SA/NSA options for RF tests but have difference for some RRM tests case which have been discussed in previous slides. So most of the work in RF group will be same for SA/NSA and the contents can be included in the same spec.
  Observation 2:
  Usually one to one mapping to RAN4 specs is good for reading and maintaining, we can use this principle as a start point. Considering the big difference between sub-6GHz and mmW in test environments and test requirements, separate specs are preferred for sub-6GHz and mmW.
  Observation 3:
  Based on the progress in RAN4, it can be expected that sub-6GHz requirements will come out earlier and RAN5 work could focus on sub-6GHz at the beginning.

## Slide 38
Issues to be discussed
  Issue 1:
  Does RAN5 need to introduce different specs for sub-6GHz and mmW for RF, demod and RRM as RAN4 discussing? If so then the spec might be:
    38.521-1a: Sub-6GHz RF, demod
    38.521-1b: mmW RF, demod
    38.521-2a: Sub-6GHz
    38.521-2b: mmW
    38.521-3a: Sub-6GHz RRM
    38.521-3b: mmW RRM
  Issue 2:
  Does test interface defined by RAN4 for mmW will affect RAN5 and at which level? If so, does RAN5 need to be involved at this stage and how to work with RAN4, joint session or LS?
  Issue 3:
  NR has introduced several new bands but a lot of LTE+NR band combinations. How to handle the relation between test case and band combinations need to be discussed. Does the test case owner is responsible for introducing all the combinations or the band combination owners introduce them to all cases as RAN4 did?

## Slide 39
Thanks