## Slide 1: WF on Enhanced CRS-IM UE Capabilities and CRS assistance
Intel Corporation
3GPP TSG-RAN WG4 Meeting #84
Berlin, Germany, 21 - 25 August 2017
Agenda Item: 7.14.1.1
R4-1709035

## Slide 2: Way Forward
Rel-14 Enhanced CRS-IM feature list
  #4-2 CRS-IM for PDSCH and 4 CRS APs for UEs with 2 RX antennas
  #4-3 CRS-IM for PDSCH and 2 CRS APs for UEs with 4 RX antennas
  #4-4 CRS-IM for PDSCH and 4 CRS APs for UEs with 4 RX antennas
  #4-5 Type A DL Control Channel IM receiver for 4 CRS APs for UEs with 2 RX antennas
  #4-6 Type A DL Control Channel IM receiver for UEs with 4 RX antennas
Reuse Rel-13 CRS-IM and DL Control Channel IM UE capabilities signalling
  UE can indicate Rel-13 CRS-IM capability (crs-InterfMitigationTM1toTM9 and ) if it supports at least one of features #4-2, #4-3, #4-4
  UE can indicate Rel-13 DL Control Channel IM Type A receiver capability (cch-InterfMitigation-RefRecTypeA-r13 and cch-InterfMitigation-MaxNumCCs-r13) if it supports at least one of features #4-5, #4-6
Reuse Rel-13 CRS Assistance signalling for Rel-14 CRS-IM
Continue discussion on possible enhancements to the CRS Assistance signalling in the TEI scope