## Slide 1: WF on Asymmetric UE CH BW operation
Dish, Intel, Mediatek, Qualcomm
3GPP TSG-RAN WG4 RAN4 #84
Berlin, Germany, August 21st-25th, 2017
R4-1709074
Agenda : 9.3.1
Document for: Approval

## Slide 2: Background

## Slide 3: Agreements to Asymmetric Channel Bandwidth operation
RAN4#83 (R4-1706321 WF on Channel Bandwidth, Qualcomm):
  The set of channel bandwidths specified in Rel-15 shall be band and SCS specific.
    Implementation and support of channel bandwidths in the specs will be done in order to minimize market fragmentation of UE.
    The maximum channel bandwidth supported by UE can be different for UL & DL and SCS specific.
RAN4 NR AH#2
  R4-1706977 WF on DL and UL CBW, Intel
    UE can support different max CBW in DL and UL
    UE can operate with different UL and DL bandwidth
  LS to RAN1 on the above agreement
    R4-1706978, “LS on downlink and uplink channel bandwidth in NR”, Intel
RAN1 NR AH#2
  R1-1711998 LS to RAN4 on Bandwidth Part Operation in NR
    For FDD, separate sets of bandwidth part (BWP) configurations for DL & UL per component carrier
      The numerology of DL BWP configuration is applied to at least PDCCH, PDSCH & corresponding DMRS
      The numerology of UL BWP configuration is applied to at least PUCCH, PUSCH & corresponding DMRS
    For TDD, separate sets of BWP configurations for DL & UL per component carrier
      The numerology of DL BWP configuration is applied to at least PDCCH, PDSCH & corresponding DMRS
      The numerology of UL BWP configuration is applied to at least PUCCH, PUSCH & corresponding DMRS
      For UE, if different active DL and UL BWPs are configured, UE is not expected to retune the center frequency of channel BW between DL and UL

## Slide 4: RAN4#84

## Slide 5: Proposals in RAN4#84
RAN4#84 – R4-1707576 Asymmetric UE UL/DL single carrier CH BW operation
  Proposal 1: For TDD, a single UL CC can be narrower than the corresponding DL CC in NR Release 15
  Proposal 2: How to apply asymmetric CH BW reference sensitivity requirements for NR bands shall be further studied during Release 15
  Proposal 3: For FDD, use the equation for delta F (ΔFTx-Rx = CBWDL/2 – CBWUL/2) to determine Tx-Rx separation in asymmetric CH BW operation in NR Release 15
  Proposal 4: Asymmetric UE UL/DL Channel Bandwidths shall be mandatory for each operating band that have requirements defined accordingly
RAN4#84 – R4-1707398 Further discussion on asymmetric DL/UL CBW (Intel)
  UEs can support different maximum channel bandwidth in DL and UL.
  UEs can operate with asymmetric UL and DL bandwidths.

## Slide 6: Agreements in RAN4#84
UEs can support different maximum channel bandwidth in DL and UL
UEs can operate with asymmetric UL and DL bandwidths
For FDD,
  ΔFTx-Rx = CBWDL/2 – CBWUL/2, defines how much Band’s default Tx-Rx separation can deviate due to asymmetric UL/DL CBW