## Slide 1: WF on MSD analysis for LTE-NR DC UE
LG Electronics
R4-1711578
3GPP TSG-RAN WG4 #84BIS Meeting
Dubrovnik, Croatia, October 09 -13, 2017
Agenda: 9.4.4.2.1 & 9.4.4.2.2

## Slide 2: MSD analysis for LTE-NR DC UE between sub-6GHz and FR1
  Agreements in R4-170724
  IMD problem :
    RAN4 should analyse MSD level for NR bands and LTE bands up to 5th IMD order to support NSA DC operation. And corresponding test configuration and MSD level will be considered to specify the NSA UE DC sensitivity level.
  Harmonic problem :
    RAN4 should analyse MSD level for NR bands up to 6th harmonic order to support NSA DC operation. From 7th order harmonic products will not have critical impact to NR sensitivity.

## Slide 3: MSD analysis for LTE-NR DC UE between sub-6GHz and FR2
  Agreements in R4-170725
  IMD problem :
    No IMD problems are expected at both LTE bands and NR bands at FR2. Hence, not necessary for study on IMD problems for LTE-NR DC UE between sub-6GHz and FR2.
  Harmonic problem :
    Not allow sensitivity degradation by the high order harmonic problem (at least 7th harmonic order) in NR bands at FR2. For the lower order harmonic problem, RAN4 need further evaluation.

## Slide 4: Way Forward
  Based on these agreements for harmonics/IMD analysis of LTE-NR DC UE, interested companies can propose MSD levels and TPs for each DC band combinations.
  The MSD level for each LTE-NR DC band combinations will be defined at next RAN4 meeting.