## Slide 1: WF on OFF power simulation assumptions for NR UE for range 2
Qualcomm Incorporated
3GPP TSG-RAN WG4 RAN#84 Bis
Dubrovnik, Croatia, October 9th-13th, 2017
R4-1711605
Agenda Item: 9.4.3.6.2

## Slide 2: Background information
UE off power for NR range 2 was discussed in RAN4 #84bis
In [1] a requirement of -25dBm TRP was proposed based on minimum coupling loss (MCL) analysis
RAN4 decided to postpone the decision to RAN4 #85 in order to have more data available to finalize the requirement
In this WF we capture the simulation assumptions to be adopted for the Montcarlo simulation

## Slide 3: Way Forward
The following simulation assumptions should be used for Montecarlo simulation:
  Indoor scenario and all related parameters as specified in TR 38.803
  Both UE to BS and UE to UE scenario can be analyzed
  Channel BW: 200MHz as baseline (other BW can be considered)
  Off power in the range of -50dBm to -25dBm should be analyzed
  Isotropic emission at UE (0dBi gain)
  BS beam as described in TR 38.803, i.e. BS is pointing at specific UEs
  Cumulative interference from all UEs to victim BS (or UE) should be evaluate
  Up to 600 Ues (50 UEs per BS) can be analyzed
  The OFF power requirement should be selected in order to achieve a maximum allowed DESENS at BS (or UE)

## Slide 4: References
R4-1710465, “OFF power requirement for NR UE for range 2”