## Slide 1: Way forward on SI reading for eFeMTC
Ericsson
3GPP TSG-RAN WG4 Meeting #84bis
Dubrovnik, Croatia, 9 - 14, October, 2017
R4-1711626

## Slide 2: Impact for specification
Core part impacted by SI requirements
  CGI reading delay requirements
Test case impacted by SI requirements
  Cell reselection
  RRC re-establishment
  Handover
  RRC redirection

## Slide 3: MIB acquisition
Companies are encouraged to investigate MIB acquisition time performance with enhanced MIB decoding
  Simulation assumption: R4-1708687, “WF on Reduced MIB Acquisition Time for efeMTC”, Ericsson, Qualcomm.
  Example of enhanced MIB decoding: R1-152190, “PBCH repetition for MTC”, Ericsson.
    Combining of MIB across consecutive MIB TTIs

## Slide 4: SIB acquisition
RAN4 will define new T_SI for Rel-15 BL/CE UE with the assumption that UE can accumulate PDSCH for SIB1/SIB2 within BCCH modification period.
  T_SI defines the time required for receiving all the relevant system information
  UE can assume that BS does not change the SIB1/SIB2 contents within the BCCH modification period.
Companies are encouraged to investigate SIB1/SIB2 acquisition time performance with the assumption above
  Simulation assumption: R4-1709004, “Way forward on SI acquisition time improvement for eFeMTC”