## Slide 1: WF on BS channel BW set
Huawei, Hisilicon, Vodafone, Ericsson
3GPP TSG-RAN4 Meeting #84bis
Dubrovnik, Croatia, 9 - 13 Oct 2017
Agenda Item: 9.3.1.3
R4-1711732

## Slide 2: Background
In RAN4 #84, WF on band specific UE channel bandwidth set (R4-1708845) was agreed.
In RAN4#84, WF on BS channel Bandwidth (CBW) set (R4-1708847) was agreed. And for new NR FR1 bands, addition of 30 MHz, 70 MHz and 90 MHz are to be decided by RAN4#84bis.

## Slide 3: Way forward on BS channel BW set in Rel-15
The same band specific channel BW set as UE is specified for BS except 3.3-3.8 GHz and 3.3-4.2 GHz band.
For 3.3-3.8 GHz and 3.3-4.2 GHz band, addition to the UE channel BWs for the band, 30 MHz, 70 MHz and 90 MHz are supported for BS. These new BS CBWs have low priority compared to the UE channel BWs.

## Slide 4: Way forward on SU for the new CBWs(30 MHz, 70 MHz and 90 MHz )
SCS [kHz] | 30 MHz | 70 MHz | 90 MHz
 | NRB | NRB | NRB
15 | 160 | N.A | N.A
30 | 78 | 189 | [245]
60 | 38 | [93] | [121]