## Slide 1: WF on LTE/NR UL subcarrier alignment
Huawei, HiSilicon, Vodafone, Deutsche Telekom, Orange, CATR, China Mobile, Etisalat, China Telecom, MediaTek, LGE, Vivo
3GPP TSG-RAN WG4 RAN#84 Bis
Dubrovnik, Croatia, October 9th-13th, 2017
R4-1711738
Document for: Approval

## Slide 2: Definitions (already endorsed)
    UL NR-LTE coexistence with UL sharing only from network perspective
    Some UEs transmit NR UL on an NR UL carrier overlapping with the bandwidth of a carrier on which other UEs transmit LTE UL
    A UE is not configured with a NR UL carrier overlapping with the bandwidth of a LTE component carrier configured for the same UE for LTE operation
    UL NR-LTE coexistence with UL sharing from UE perspective
    A UE is configured with a NR UL carrier overlapping with the bandwidth of a LTE component carrier configured for the same UE for LTE operation
      E.g. a UE supports transmitting NR UL and LTE UL within the bandwidth of an LTE component carrier configured for the UE

## Slide 3: Background
It was agreed that LTE/NR UL subcarrier alignment is to be specified by Dec 2017 in RP-172104, “Way forward on UL sharing aspects” at RAN#77.
To achieve LTE/NR subcarrier alignment, the following options are possible
  Option 1: Base band shift with 7.5kHz shift, without requiring LO frequency retuning, applicable to both shared and independent RFs
  Option 2: Digital rotator with 7.5kHz, without requiring LO frequency retuning , applicable to both shared and independent RFs
  Option 3: RF shift with independent RFs, without requiring LO frequency retuning
  Option 4: RF shift with shared RFs, requiring LO frequency retuning

## Slide 4: Way forward based on
R4-1710742 PLL lock time; ZTE Corp.
R4-1710862 Discussion on LTE/NR Uplink subcarrier alignment; LGE
R4-1710884 On UL sharing related shifting time between LTE and NR for NSA UE; Intel Corp.
R4-1711319 Subcarrier alignment for LTE/NR uplink coexistence; Huawei Technologies

## Slide 5: WF proposal
For UL sharing from network and UE perspective with LTE/NR UL subcarrier alignment, the switching time between LTE and NR shall be minimized to guarantee system performance.
  In order to allow different implementations e.g. Digital rotator (~0us), RF shift (<20us), UE switching time between LTE and NR shall be defined as UE capability with the two options ~0us and <20us.
  For a UE reporting capability of “~0us” the switching time between LTE and NR is ~0us in all UL sharing cases except the following case:
    The UE is using UL sharing from UE perspective with the UL CBW for LTE and NR being different OR NR UL uses SCS =60KHz, the switching time is FFS
  For a UE reporting capability of “<20us” the switching time between LTE and NR is below 20us in all cases
  RAN4 shall define the corresponding requirements for this switching time
  Note: UE switching time includes LO re-tuning time and any additional related interruption time due to RF and BB transition between LTE and NR, excluding the normal LTE transient period (20us) or NR transient period (10us), which will be captured in the time mask requirement.
Send an LS to RAN1/2 capturing the above agreement. This LS is not intended to change the RAN1 agreement in R1-1711839

## Slide 6: More detailed info on implementation options
Option 1 will be precluded due to RAN1 impact.
It is understood that there could be more options than the fourthree listed here(option 2/3/4).

## Slide 7: Option 1: BB shift
Tx HF
LTE BB ASIC
NR BB with 7.5 kHz shift ASIC
LTE/NR
Modem
LTE/NR
RF IC
RF@
1.8 GHz
Switch
DAC
RF@
3.5 GHz
DAC
Tx LF
3.5 GHz
1.8 GHz
PLL
PLL
PA@1.8GHz
PA@3.5GHz
LTE
RF IC
Tx LF
Tx HF
LTE
BB ASIC
NR BB with 7.5kHz shift
ASIC
LTE
Modem
RF@
1.8 GHz
Switch
DAC
RF@
3.5 GHz
DAC
RF@
1.8GHz
DAC
PA@1.8GHz
PA@3.5GHz
NR
Modem
NR
RF IC
RF other band
…
BB shift is applicable to implementations with either shared or independent RF for LTE/NR at the shared carrier
BB shift does not require LO frequency retuning and minimizes the LTE/NR switch time

## Slide 8: Option 2: Digital rotator
LTE
RF IC
Tx LF
Tx HF
LTE
BB ASIC
NR BB
w/o 7.5kHz shift
ASIC
LTE
Modem
RF@
1.8 GHz
Switch
DAC
RF@
3.5 GHz
DAC
RF@
1.8GHz
DAC
PA@1.8GHz
PA@3.5GHz
NR
Modem
NR
RF IC
RF other band
…
Tx HF
LTE BB ASIC
NR BB
w/o 7.5 kHz shift ASIC
LTE/NR
Modem
LTE/NR
RF IC
RF@
1.8 GHz
Switch
DAC
RF@
3.5 GHz
DAC
Tx LF
3.5 GHz
1.8 GHz
PLL
PLL
PA@1.8GHz
PA@3.5GHz
7.5kHz digital rotator
7.5kHz digital rotator
Digital rotator is applicable to implementations with either shared or independent RF for LTE/NR at the shared carrier
Digital rotator does not require LO frequency retuning and minimizes the LTE/NR switch time

## Slide 9: Option 3: RF shift with independent RFs
RF shift with independent RFs does not require LO frequency retuning and minimizes the LTE/NR switch time
Tx HF
LTE BB ASIC
NR BB w/o 7.5kHz shift ASIC
LTE/NR
Modem
LTE/NR
RF IC
RF@
1.8 GHz
DAC
RF@
3.5 GHz
DAC
Tx LF
PA@1.8GHz
PA@3.5GHz
RF@
1.8000075 GHz
DAC
PA@1.8GHz
+7.5kHz

## Slide 10: Option 4: RF shift with shared RFs
RF shift with shared RFs requires LO frequency retuning and degrades the system performance
Tx HF
LTE BB ASIC
NR BB w/o 7.5kHz shift ASIC
LTE/NR
Modem
LTE/NR
RF IC
DAC
RF@
3.5 GHz
DAC
Tx LF
PA@3.5GHz
RF @ 1.8GHz or 1.8000075 GHz
PA@ 1.8GHz or 1.8GHz +7.5kHz