## Slide 1: 3GPP TSG-RAN WG4 Meeting NR84bis
ZTE, Ericsson, Huawei
WF on Operator Protection in EMC Specification
R4-1711834

## Slide 2: Background
Based on the discussion in [1][2], the EMF exposure will exceed the ICNIRP limit during EMC test for Range 1-O and Range 2 NR BS if the test operator stands near the EUT.
Most of the Range 1-O and Range 2 NR BS immunity testing can be implemented inside the anechoic chamber to prevent the EMF exposure except for the electrostatic discharge (ESD) immunity test.
For the electrostatic discharge (ESD) immunity test, due to test operator needs to use the ESD simulator and stand very close to the EUT, therefore some possible methods should be considered to ensure the test operators’ safety to avoid large EMF exposure, which are listed as follow[2]:
  Option 1: Test the NR BS in receiver mode only.
  Option 2: Set the NR BS transmitting in a feasible low power which is safe to the perator.
  Option 3: Implement ESD immunity test with a robot arm in the anechoic chamber.

## Slide 3: WF Agreement
Tests listed below will be aligned with the conformance part of the technical specification TS 38.113: conducted emission, harmonics current emission, voltage fluctuations and flicker emission, electronic fast transients immunity, surge immunity, conducted immunity, voltage dips and interruptions immunity.
  Configuration of operator protection in EMC is FFS.
2. To protect the test operator in ESD immunity tests for Range 1-O and Range 2-O NR BS, different options are considered:
  Option 1: Test the NR BS in receiver mode only.
  Option 2: Set the NR BS transmitting in a feasible low power which is safe to the operator.
  Option 3: Implement ESD immunity test with a robot arm in the anechoic chamber.
  Other options are not precluded.

## Slide 4: References
[1] R4-1710559, Discussion on EMF Exposure of NR BS. ZTE
[2] R4-1710560 , Consideration on test configuration for NR BS EMC testing, ZTE