## Slide 1: WF on measurement capability and measurement gap for NR
Intel
3GPP TSG-RAN WG4 RAN#84 Bis
Dubrovnik, Croatia, October 9th-13th, 2017
R4-1711887
Document for: Approval

## Slide 2: Agreement on UE capability for FR1/2 measurements
Recommend to introduce UE capability to indicate
  Independent measurement gaps can be supported for FR1 and FR2 measurement objects respectively. That includes the case the configured measurement gaps are identical for FR1 and FR2 Or
  Single measurement gap can be configured per UE
Recommend RAN2 to introduce the related signaling best effort based
To do in RAN4#85: introduce measurement gap based requirements for per-UE based measurement gap and FR1/2 independent measurement gap (best effort based)

## Slide 3: Agreement on MGL
For UE supports single and per UE gap, three MGL are introduced, 6ms, [4]ms and 3ms
For UE support independent gap for FR1/2, the following MGL are introduced
  FR1 measurement objects: 6ms, [4]ms and 3ms
  FR2 measurement objects:
    With FR1/LTE serving cell only: 6ms, [4]ms and 3ms
    With FR2 serving cell:
      If identical gap is configured for both FR1 and FR2: 6ms, [4]ms, 3ms,
      If independent gap is configured for FR1 and FR2:[1+x] ms, [2.5+x] ms, [5+x]ms
    Note: x is defined based on RF switching time and TBD in RAN4#85
    Non-NR-capable UE does not need to support new gap other than 3ms or 6ms

## Slide 4: Agreement on MGRP
Four MGRP to be introduced: 20ms, 40ms, 80ms and 160ms for NSA and SA NR UE
  If non-NR measurement objects are configured, 160ms MGRP should not be used
  40ms MGRP LTE requirements will apply if 20ms MGRP common gap is configured
  Use of 20ms MGRP configured by LTE PCell needs update to gap pattern IDs supported in 36.133
  Updates are needed in 36.133 on use of 20ms MGRP applicability, non uniform applicability, NCSG applicability etc
  For UE not supporting NR, both 20ms and 160ms should not be configured
Necessity of 20ms MGRP +6ms MGL to be confirmed by RAN4#85
To do in RAN4#85:
  Identify the combinations of MGRP and MGL, which are necessarily to be introduced in Rel-15
  Update measurement gap configuration table based on updated MGL and MGRP

## Slide 5: Agreement on intra-frequency measurements for FR2
It shall be assumed in release 15 that all UE are not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on FR2 serving cells during FR2 intra-frequency measurements, ie no capability is needed
For UE not supporting mixed numerology scenarios in FR1 and FR2, UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH for intra-frequency measurement without RF-retuning
SMTC or gap based measurements may be considered by RAN4
  Conditions for SMTC or gap based measurement are FFS
With inter-frequency or gap based mixed numerology or intra-frequency with measurement gap, gap is shared for all FR2 measurements
To do in RAN4#85: depending on UE capability, further investigate how to handle intra-frequency with no RF-retuning in both FR1 and FR2
  For example: SMTC based mechanism

## Slide 6: Agreement on inter-frequency measurements
For FR2, gaps are needed due to RX beamforming assumption by network which is also applicable for intra-frequency measurement.
For FR1, gaps are needed for inter-frequency measurements
  if UE indicates the capability of measurement without gap, gap is not needed.
  needforGaps signaling is benefitial be extended to NR+LTE NSA operation.

## Slide 7: Agreements on mixed numerology related measurements
When target SSB is within UE’s active BWP
  If UEs does not support FDM mixed numerology between SSB and non-SSB RE of serving cell, it is FFS if measurement gap based or SMTC based mechanism is needed for intra-frequency measurements.
  If UE supports FDM mixed numerology between SSB and non-SSB RE, measurement gap or SMTC based mechanism is not needed.
  This applies to both serving and target cells
  Capability is needed.
In case gaps are needed on FR2 serving cell(s) for other purpospurposes(es) (e.g. interfrequency measurements), RAN4 assumption is that a single gap pattern will be shared for FR2 RX beamformed measurements and the other purpos(es) including intra-frequency measurement without RF retuning.
  To do in RAN4#85: depending on UE capability, further investigate how to handle intra-frequency with no RF-retuning in both FR1 and FR2
  For example: SMTC based mechanism

## Slide 8: Agreements on measurement gap configuration
RAN4 is still discussing if gap or other mechanism is used for
  Intrafrequency measurements within the active BW part on FR2 due possible RX beamforming
  Intrafrequency measurements within the active BW part with a different numerology between data/control and SS block
  To do in RAN4#85: study other mechanisms on how to handle intra-frequency with no RF-retuning in both FR1 and FR2

## Slide 9: Agreements on gap sharing
Gap sharing between intra-frequency with gap and inter-frequency measurement
  Configurable by NW with up to 4 levels including equal sharing