## Slide 1: Proposal for MIMO OTA TRMS requirements
NTT DOCOMO INC., SGS Wireless
3GPP TSG-RAN WG4 Meeting #84bis R4-1713075
Reno, USA, 27 Nov. - 1 Dec., 2017
Agenda item: 6.2
Document for: Approval

## Slide 2: Background
4-bands requirements (band 1, 7, 39, 41) are defined.
Some bands are still remained in PS1.
Additional test results are provided [R4-171xxxx], MIMO OTA TRMS results for band 3, 5, and 19 are available (>15 DUTs) and the CDFs are analyzed;
Based on the agreed framework [R4-1706413], Potential requirement value can be developed. The details are shown in next slide.

## Slide 3: Investigation of the potential value
Based on the agreed framework [R4-1706413], Potential value is follows. (derived from 85 +/-5% value of CDF)
For Band 3, some potential requirement value was proposed in the last meeting. After some off-line discussion, potential value is remained to be checked by each company.
Band | TRMS_70 limit |  |  | TRMS_95 limit |  | 
 | 80% value of CDF | 85% value of CDF | 90% value of CDF | 80% value of CDF | 85% value of CDF | 90% value of CDF
3 | -96.0 | -94.9 | -94.7 | -94.1 | -92.8 | -92.5
5 | -94.7 | -94.6 | -94.3 | -92.7 | -92.7 | -92.6
19 | -95.6 | -95.3 | -95.1 | -93.5 | -93.3 | -93.2
 | TRMS_70 limit | TRMS_95 lim
R4-1710391 | -93 | -91
R4-1711419 | -94.2 | -92.2
DOCOMO view (on-line comment) | -94.25(same as B1) | -92.25(same as B1)

## Slide 4: Proposed requirements
Values in table below should be approved as MIMO OTA TRMS requirements in free space configuration:
For band 3, comparing CDF value, below proposal is relaxed. But, we respect the discussion of the last meeting and keep the potential value of the discussion.
For low band requirement, below values are rounded from CDF value of 85%.
Band | RS-EPRE Unit | TRMS | 
 |  | Average, 70 | Average, 95
3 | dBm/15 kHz | -93.75 | -91.75
5 | dBm/15 kHz | -94.5 | -92.5
19 | dBm/15 kHz | -95.25 | -93.25