## Slide 1: Way forward on eFeMTC RRM requirements under CRS muting
Ericsson
3GPP TSG-RAN WG4 Meeting #85 R4-1713161
Reno, Nevada, US, 27 November – 1 December, 2017
Agenda Item: 8.21.4.2

## Slide 2: Background
Release 15 MTC WI includes the following objective:
  Introduce capability signaling for support for CRS muting outside BL UE narrowband/wideband [RAN1 lead, RAN2, RAN4]
    Enable BL UE to optionally indicate that it does not rely on CRS outside its narrowband/wideband +/- X PRBs, where X is determined by RAN1 and RAN4.
Based on this objective, RAN4 has discussed RRM requirements and made some progress. In this way forward, we capture the agreements on remaining open issues on RRM requirements.

## Slide 3: Proposals
CRS transmissions light up
  CRS transmissions are switched ON over full BW in 1 DL subframe every 20 ms.
Warm up period
  Warm up period for UEs in CEModeB is defined as 2 DL subframes.
CRS transmission BW for Cat-M2
  CRS transmission BW in the center frequency and corresponding UE timing requirements are defined as follows:
Pre-provisioning of muted carriers
  Signaling of EARFCN of the muted carriers together with location, timing and muted information can enhance the UE operation.
CRS transmission BW in the center frequency | CRS transmissions BW within UE BW in warm-up subframes [RB] | UE Doppler frequency (V) | Timing error (Te_)
6 RBs | 24 | V < 220 Hz | 12*Ts
24 RBs | 24 | V ≥ 220 Hz | 12*Ts

## Slide 4: Proposals on positioning
RSTD measurements
  When CRS muting is used with eFeMTC, CRS shall not be muted in PRS subframes within the UE bandwidth in the measured cell and the existing FeMTC RSTD requirements shall apply.
UE Rx-Tx measurements for E-CID
  For UE Rx-Tx time difference measurements, the existing requirements apply provided CRS are available within the UE bandwidth in the serving cell during the UE Rx-Tx measurement period.
RSRP and RSRQ measurements for E-CID
  For RSRP and RSRQ measurements for E-CID, the same principles with respect to CRS muting apply as for general RRM measurements in RRC_CONNECTED.
Positioning measurements by HD-FDD
  CRS shall be assumed within the UE bandwidth in the serving cell during UL transmission gaps, and
  Central 6 RB CRS within the serving cell BW can be assumed during UL periods regardless of DRX/non-DRX, except for the UL transmission gaps.