## Slide 1: WF on MPR for PC6 MTC
Ericsson
3GPP TSG-RAN4 Meeting #85
Reno, US, 27 Nov - 1 Dec 2017
R4-1713980

## Slide 2: Proposals
For CAT-M2 PC6 MTC, MPR result integration with E/// (R4-1713081) and QC result (R4-1713579) is proposed to take following factors:
  1) MPR table need to consider the NB index allocation in different system bandwidth
  2) The length of the continuous PRB need to follow the RAN1 spec: The continuous length of the PRB acc. to 36.212(:5.3.3.1.10), 36.213( 8.1, 8.1.5, 8.1.5.1) is [1, 2, 3 4, 5 6, 9, 12, 15 ,18, 24]
  RBstart is indexed within the allocated NB bandwidth.
For CAT-M2 PC6 eMTC, MPR CR will be provided next meeting

## Slide 3: Proposals
For CAT-M1 PC6 eMTC, MPR table for low output power CAT-M1 will be proposed next meeting.
No A-MPR needed for PC6 CAT-M1 device with current supported frequency band. The frequency band is below (acc. to 36.101 V15.0.0):
  UE category M1 and M2 is designed to operate in the E-UTRA operating bands 1, 2, 3, 4, 5, 7, 8, 11, 12, 13, 14, 18, 19, 20, 21, 25, 26, 27, 28, 31, 66, 71, 72 and 74 in both half duplex FDD mode and full-duplex FDD mode, and in bands 39, 40 and 41 in TDD mode.
No A-MPR needed for PC6 CAT-M2 device with current supported frequency band except NS_07, NS_15, NS_07, NS_15 need further investigation.
  UE category M1 and M2 is designed to operate in the E-UTRA operating bands 1, 2, 3, 4, 5, 7, 8, 11, 12, 13, 14, 18, 19, 20, 21, 25, 26, 27, 28, 31, 66, 71, 72 and 74 in both half duplex FDD mode and full-duplex FDD mode, and in bands 39, 40 and 41 in TDD mode.